## Slide 1: PowerPoint 11: Understand how to install plasterboards and timber laths: Tools and equipment
PowerPoint presentation
Unit 109: Plastering and interior systems

## Slide 2: Plasterboard hand tools
Notes: Set Worksheet 41

## Slide 3: Power tools
Portable power tools for fixing plasterboards to timber and steel backgrounds.
Types of voltage.

## Slide 4: Struts and lifters
Equipment used for positioning plasterboard before fixing.
Notes: Set Worksheet 42

## Slide 5: Fixing plasterboard
Plasterboards are manufactured from gypsum, sandwiched between lining paper on both sides.
They are used as a background surface in new and traditional buildings to form a dry construction background known as ‘dry lining’.
Plasterboard provides a ﬂat surface that can be plastered or jointed.
Plasterboard has been manufactured as an alternative to traditional timber lath.
Performance plasterboard is manufactured in line with building regulations.
Fixed to timber and metal background.

## Slide 6: Plasterboard
There are three manufacturing companies that manufacture plasterboard.
Building regulations govern which type of plasterboard is used. Plasterboard is manufactured in a range of sizes. The most common:
2.400m x 1.200m, thickness 9.5mm, 12.5mm, 15mm and 19mm.
1.800m x 0.900mm, thickness 9.5mm and 12.5mm.
Plasterboard is either square or tapered edge, often abbreviated to ‘SE’ and ‘TE’.
Performance plasterboard is designed to meet various requirements and is colour-coded.

## Slide 7: Performance plasterboard
This is plasterboard that has additional characteristics compared with standard plasterboard and can increase the performance of a room:
Sound insulation
Fire resistance
Moisture
Insulation.
Notes: Set Worksheet 43

## Slide 8: Storing plasterboard
Plasterboard should be delivered ﬂat on pallets or on timber bearers.
Manufacturer data sheets provide speciﬁc information about storing and manual handling of materials and components.
Plasterboard is best carried on its edge by two people to prevent the board snapping.
Plasterboard should not come into contact with damp conditions as the plaster core will absorb the moisture.
Different types of plasterboard should be stored separately to avoid confusion.
Plasterboard waste can be recycled.

## Slide 9: Fixing with screws
Drywall screws are considered stronger ﬁxings than galvanised nails and have less chance of popping through the ﬁnished surface.
Fixing with screws means the plasterboard surface is less likely to move under vibration and twisting or moving timber.
Screws must penetrate the timber by a minimum of 20mm. They have less thread and give a stronger grip into the timber background
Screws must penetrate the steel stud or lining by 10mm. They have a closer thread that gives a strong grip into thin metal linings.

## Slide 10: Fixings with galvanised nails
Plasterboard is supported by ﬁxings, fixed every 150mm.
Galvanised nails have protective zinc coating applied to steel to prevent corrosion or rusting.
Thickness of board Minimum size of nail
9.5mm 30mm
12.5mm 40mm
15mm 40mm
19mm 50mm

## Slide 11: Dry wall screws
Screws are fixed at 230mm for studs and 300mm for ceiling joists.
Size of board Minimum size of screw
12.5mm 38mm
15mm 41mm
19mm 51mm
12.5mm Double layer 51mm
Collated screws are ﬁxed using a mechanical drywall auto feeder. Collated screws vary in length from 25mm to 50mm.

## Slide 12: Dry wall screws
Fixing to metal studs or furrings
Size of board Minimum size of screw
9.5mm 22mm
12.5mm 25mm
15mm 25mm
19mm 42mm
12.5mm Double layer 36mm

## Slide 13: Fixing centres
Joist/stud centres must be able to take the weight of the plasterboard. Joists that are too far apart will cause the plasterboard to sag.
Centres: distance between two joists or studs.
Noggin: timber ﬁxed between joists or studs to support.
Plasterboard Centres Centres with noggins
12.5mm 600mm 450mm
15mm 600mm 600mm
19mm 600mm 600mm
Thermal laminates 600mm 450mm

## Slide 14: Fixing plasterboard to ceilings
Before you start, all services including ducting, pipes and cables should have been installed (first fix).
Considerations.
Setting out.
Fixing procedure.

## Slide 15: Fixing plasterboard to studs
There are two methods that can be used when ﬁxing plasterboard to studwork.
Plasterboard can be fixed horizontally or vertically in line with the studs.
Considerations.
Setting out.
Fixing procedure.

## Slide 16
When fixing plasterboards to frame walls, it is advisable to stagger the boards on the opposite side of the wall. This will strengthen the wall and distribute the weight and stress.
Fixing plasterboards
Plasterboard
Joint fixed to this stud
Joint fixed to this stud
Stud
Notes: Set Worksheet 44

## Slide 17: Fixing timber laths
Types of lath materials:
Riven (split) or sawn. Riven is stronger as it reduces short grain and retains its inherent strength.
Oak, chestnut or larch – in order of strength.
Fixing
Timber laths should be fixed with stainless steel nails (traditionally hand-cut wrought iron nails) with 10mm spacing.
It is advisable to stagger joints at approximately 1m distance, to provide stability and prevent creating ‘ladders’.

## Slide 18
Any questions?