## Slide 1: PowerPoint 2: The responsibilities of a plasterer
PowerPoint presentation
Unit 109: Plastering and interior systems

## Slide 2: Maintain plastering tools and equipment
Check the quality of tools and equipment before you start
Cleaning tools and equipment
Safe storage of tools and equipment
Power tools for mixing and installing plasterboard
Mechanical tools

## Slide 3: Setting up a safe mixing area
When mixing plaster, the first thing to do is set up your mixing area with the necessary tools.
The mixing area should:
have plenty of ventilation
have access to clean water and electricity
be as close as possible to the stored material
have an area for disposing of waste materials
have protective floor coverings if required.

## Slide 4: Protecting surfaces before plastering
Notes: Set Worksheet 5

## Slide 5: Carry out checks on mixing materials
Before mixing materials you will need to check the following.
Quality of material.
Storage and protection of materials.
Age and condition.
Contamination.
Water for mixing must be clean.
Mixing equipment
If plastering materials are mixed by hand or mechanical means.

## Slide 6: Traditional loose plastering materials
Traditional loose plastering materials include:
Aggregate, binders, reinforcements and additives
Lime-based plaster
Sharp sand mixed with hydraulic lime and horse or goats hair reinforcement
Cement-based backing plaster
Ordinary Portland Cement mixed with building sand and plasticiser/waterproofer.

## Slide 7: Lightweight pre-blended binders and aggregates
Backing plasters contain vermiculite and perlite aggregate mixed with gypsum binder.

## Slide 8: Lightweight pre-blended gypsum backing plaster

## Slide 9: Finishing plaster

## Slide 10: Manufacturer’s plastering information
Gypsum plaster contains manufacturer's instructions which provide guidelines on how to use the plaster product.
Always check the use-by date on bagged plaster to avoid fast or slow setting.
There are advantages and disadvantages of pre-blended plaster compared to traditional.

## Slide 11: Plasterboard
Plasterboard is made of gypsum plaster set between two sheets of paper, used especially to form or line the inner walls of houses.
You will need to know about:
storing
manual handling
defects
recycling waste.

## Slide 12: Plastering specification
A plastering specification will include the following information.
Description of the plastering materials to be used.
Preparation of background substrates.
Applied plaster thickness including application layers.
Strength and consistency achieved by measuring and gauging to ratios.
Standards of workmanship.
Notes: Set Worksheet 6

## Slide 13: Preparing backgrounds for plastering
Different backgrounds need to be prepared for plastering in different ways. There are several steps that you need to follow to make sure the plaster adheres well to the surface:
assessing strength and condition
controlling suction
forming a key
forming a mechanical key
applying bonding agents.
Notes: Set Worksheet 7

## Slide 14: Safe working
Before starting any work, you must be familiar with the risk assessment and method statement. To work safely you will need to do the following.
Complete a workplace induction.
Wear appropriate PPE.
Understand and follow housekeeping rules.
Check all equipment before use.
Know evacuation procedures.
Understand first aid procedures.
Know how to work at height safely.
Understand accident reporting and recording procedures.

## Slide 15: Environmental considerations
You will need to be aware of the following environmental considerations:
how to clean tools, equipment, work and dispose of waste
type of plastering waste.
waste recycling
segregation of waste.
effect of hazardous waste on the environment.
Notes: Set Worksheet 8

## Slide 16
Any questions?