## Slide 1: PowerPoint 6: Tools for preparing different backgrounds for plastering work
PowerPoint presentation
Unit 109: Plastering and interior systems

## Slide 2: Forming a key
Forming a key means creating a rough surface to improve its adhesion
Forming a key for plaster is one of the most important jobs a plasterer can do. Failing to provide a key will result in bond failure and the plaster falling off the wall.

## Slide 3: Tools and equipment used for preparing backgrounds
New work requires little preparation when applying plaster to backgrounds. However, when renovating older properties you will need to ensure existing surfaces have sufficient key, allowing plasters to bond.
Some surfaces have poor key or no key and will need to be prepared using different tools and methods.
Notes: Set Worksheet 21

## Slide 4: Lump hammer and bolster
The lump hammer is knocked against the head of the bolster to remove old plaster from backgrounds.

## Slide 5: Removing defected plasterwork
Removing old plaster from backgrounds is a process known as ‘hacking’.
It is important to remove all loose plaster from the surface. This can be carried out by hand or mechanically using various tools and equipment.

## Slide 6: Scutch hammer
This hammer has sharp teeth and can be used for removing plaster. It leaves a rough surface on backgrounds.

## Slide 7: Pick hammer
This hammer has a flat end on one side and a pointed end on the other. It is a good tool for getting in between thin, tight surfaces like brick and stone to rake out the joints.

## Slide 8: Claw hammer
This hammer is used when preparing timber backgrounds that have been previously plastered. Its main function is to remove old nails that might be left in the timber surface, or to remove old lath work or damaged plasterboard.

## Slide 9: Nail bar used to remove nails in timber

## Slide 10: Lath hammer
A traditional tool used by plasterers, before plasterboard was widely used, to cut wooden laths when lathing. Also used for hacking off old sand–lime plaster from walls.
Notes: Set Worksheet 22

## Slide 11: Bonding agents
Spatterdash slurry was a traditional method for bonding surfaces: cement and sharp sand made into a slurry and then thrown onto the background with a paddle or small shovel. In more recent years, PVA or SBR is added to increase and improve the slurry’s bonding properties.

## Slide 12: Applying a bonding slurry with a brush
Mix the dry slurry with water and apply direct to the surface with a brush, then stipple the surface to create a textured finish that forms a good key. This type of slurry is left for 24 hours to go hard before cement-based plaster is applied.

## Slide 13: Roller and tray used for applying bonding grit
There are many new products for bonding plasters on the market today that have been developed in laboratories. For example, ThistleBond-it and Febond Blue Grit have been developed for over skimming solid surfaces. You can apply these adhesives with a soft brush or roller.

## Slide 14: Grit bonding adhesive
There are many new products for bonding plasters on the market today that have been developed in laboratories. For example, ThistleBond-it and Febond Blue Grit have been developed for over skimming solid surfaces. You can apply these adhesives with a soft brush or roller.

## Slide 15: Used on high suction backgrounds
Notes: Set Worksheet 23

## Slide 16: Floor scrapers
A floor scraper is often used with a sweeping brush for cleaning the work area during and after applying the scratch coat. Wet plastering materials can cause a slippery surface and need to be cleared up as soon as possible to prevent slips.

## Slide 17: Mechanical breaker
A breaker is a heavy-duty power tool generally used on hard, stubborn areas of plaster that are difficult to remove by hand using just a hammer and bolster.

## Slide 18: Transformer
All electrical power tools on site need to be run on the recommended voltage of 110 volts. You can step down the voltage from 230V to 110V using a transformer; this will make it safer to use.

## Slide 19: Scoring a surface with a grinder

## Slide 20: Needle gun attachment for removing flaking paint

## Slide 21: Resources
Notes: Set Worksheet 24

## Slide 22
Any questions?