## Slide 1: PowerPoint 12: Identify and understand how to fix plastering beads
PowerPoint presentation
Unit 109: Plastering and interior systems

## Slide 2: Types of areas for fixing beads
Window wall with returns
Walls with door ways
Walls with corner returns
Chimney walls
Independent piers
Beams
Bulk head soffits
Splayed angles
Notes: Set Worksheet 45

## Slide 3: Beading
Metal angle beads are used to form straight arrises that are resistant to normal damage.
Timber P beads should be used on lime plaster instead of metal beads.

## Slide 4: Thin coat beads
Thin coat angle beads can be fixed to solid or plasterboard corners.
Thin coat stop bead.

## Slide 5: Stop bead
Metal stop beads are used to form straight stops to plaster.

## Slide 6: Movement bead
Used to allow for movement in the building.
Used on high or long walls.

## Slide 7: Corner movement bead
To allow for different shifting between walls.
Allows movement to prevent cracking.

## Slide 8: Feature bead
Usually fixed around door frames and openings.
Stops the plaster from coming into contact with the frame.
Provides a shadow effect.
Notes: Set Worksheet 46

## Slide 9: Tools for fixing beads
Marker
Tape measure
Snips
Level and straight edge
Square

## Slide 10: Fixing beads
Standard angle beads are generally fixed with plaster dabs because it is a fine material that allows the mesh wing of the bead to bed into the plaster.
Dabs are placed every 400mm approximately.
Cutting back.
Note that gypsum plaster dabs should not be used with lime plaster and steel angle-beads can weaken lime plaster.

## Slide 11: Window walls
Setting out and positioning and fixing beads to a window wall.
Always check for plumb, level, correct dimensions, margins and square.
Notes: Set Worksheet 47

## Slide 12: Checking beads for accuracy
Beads should be fixed in-line straight
Plumb
Level
Square
Correct dimensions
Equal margins
No steps
Cut back
Left clean and sharp

## Slide 13
Forming hard angles
Sometimes an external angle needs to be created without the use of pre-formed beads.
This may be necessary when matching existing angles or if specified (perhaps for heritage work).

## Slide 14
Traditional hard angles

## Slide 15
Square arris
Formed by the reverse rule method.
Most common type of hard angle.

## Slide 16: Forming hard angles
Timber rule: a straight plane timber used as a guide.
Hard angles are commonly used in conservation and renovation work on uneven backgrounds.
Blockwork
Soffit
Reveal
Level
Window opening
Using timber rules in a window

## Slide 17: Square arris
Skimming can be applied and finished with the aid of an external angle trowel.
Notes: Set Worksheet 48

## Slide 18
Any questions?