## Slide 1: PowerPoint 9: Identify and recognise different methods for planning the sequence of work
PowerPoint presentation
Unit 109: Plastering and interior systems

## Slide 2: Aims
Interpret and extract construction information and documentation with regards to planning, preparing, mixing, installing and finishing internal plastering systems using:
Drawings
Specifications
Schedules
Manufacturer's information
Building regulations.

## Slide 3: Drawings
Before you carry out plastering work, you need to study the relevant working drawings. These provide valuable information to help you successfully complete the work to the standards required in the contract agreement.
When reading drawings, it is important to report as soon as possible anything that you think is a mistake, in case it causes more problems at a later stage.
Mistakes must be reported to someone in higher authority, who will then contact the architect and ask them to correct the problem.
Learning about the different drawings will ensure you can work to the correct standards.

## Slide 4: Block plans
Block plans show the proposed development in relation to its surrounding properties.
Sand St
Green St
Plot 1
Plot 2
Plot 3
Scale: 1:200

## Slide 5: Floor plans
    Show the positioning of wall and sizes of rooms, along with the positioning of elements within the building such as units.
    Layout drawings can be used for calculating internal plastering materials.

## Slide 6: Reflective drawings
    Provide dimensions of ceilings
    Provide the dimensions for the centres of joists.

## Slide 7: Elevation drawings
Elevation drawings show how each individual wall is seen, whether they are plain walls or have windows and/or door openings. You can refer to these drawings when measuring openings for doorways and windows, or when checking whether the background walls contain different properties, such as lintels or wall plates.

## Slide 8: Detailed drawings
Detailed drawings show details of construction, normally as a cross-section.
Wall plate
Plaster dabs
Brickwork
EML
Standard angle bead

## Slide 9: Specifications
The specifications document provides specific information about the type of plastering material to be used.
It will provide the make and manufacturer of plaster/sheet material or type of bead.
It will also provide details of the thickness of application or thickness of sheet material.
The specification will accompany the drawing and specify the standards of workmanship.
You will need to refer to the specification when estimating quantities and costs of materials for the plastering work.

## Slide 10: Learner feedback
Specification spider gram

## Slide 11: Material schedules
There are two types of schedules that are referred to in the construction industry.
A plastering schedule: lists how many bags of pre-mixed backing and finishing plaster are required, the number of different beads or number of performance plasterboards that are required for the different rooms in the development.
Labour schedule (sometimes called a ‘programme of work’ or ‘work schedule’): a list of planned work activities to be completed in a sequence to avoid congestion of labour.
This document provides a list of repeated building materials for similar developments.

## Slide 12: Manufacturer’s information
Manufacturers’ documents provide specific information on the plastering product to be installed.
Manufacturer information provides user guide information on safety, storage, mixing and installation instructions.
When working with materials, it is imperative to refer to the manufacturer’s instructions to ensure the product is installed as instructed, therefore ensuring the warranty remains intact.
Manufacturers of plaster and plasterboard provide these data sheets on their websites.

## Slide 13: Storing plastering materials
Bagged materials
Loose materials
Containers
Beads
Laths and reinforcements
Sheet materials
Components
Fixings

## Slide 14: Building regulations
Building regulations govern the standards of workmanship and regulate a standard building practice throughout the UK. This will ensure that all buildings built under building regulations conform to the same performance and standards.
Part C resistance to contamination and moisture
Part E resistance to sound
Part B resistance to fire
Part L conservation of fuel and power
These documents provide general guidance of the performance expected from plastering materials to meet building regulations (see www.gov.uk/government/collections/approved-documents).

## Slide 15
Any questions?