## Slide 1: PowerPoint 10: Preparation materials
PowerPoint presentation
Unit 110: Decorative finishing and industrial painting occupations

## Slide 2: Abrasives
It is important to select the correct type and grade of abrasive paper when rubbing down.
Too coarse and it may scratch or damage the surface
Too fine and it will not be effective and clog easily
There are many types of abrasive paper. The two most common types used by painters and decorators are:
aluminium oxide
silicon carbide (wet or dry)
Notes: LINKED TO WORKSHEET 8

## Slide 3: Aluminium oxide
Quicker and more effective than other types of dry abrasives
Less clogging than traditional ‘sandpaper’
Sold in 5, 10 and 50 metre rolls
Readily available
Produces dust
Durable
GRADES: Rough to smooth 40 ,60, 80, 100, 120

## Slide 4: Silicon carbide (wet or dry)
Can be more effective than dry abrading
Not suited to porous surfaces
Materials are more costly
Wide selection of grades
Does not produce dust
Can be messy
GRADES: Rough to smooth 120....220....360....400....600
      .

## Slide 5: Filling materials
    The type of filling materials used will normally depend on the surface being filled. There are many types of filling materials:
    interior and exterior powder or ready mixed filler
    ready mixed coloured wood filler
    ready mixed fine surface filler
    two pack filler
    caulk

## Slide 6: Powder filler
Plaster-based filler used to repair and make good interior surfaces such as plaster, wood, plasterboard. It is normally white.
Cement-based filler is normally grey, and is cement based, used on exterior render.

## Slide 7: Ready mixed filler
There are many types of ready mixed fillers, all with different uses.
Coloured wood filler for use before applying varnish
Flexible paste fillers for cracks subject to movement
All purpose filler for general small repairs
Lightweight filler for general filling
Fine surface filler for face filling

## Slide 8: Two pack filler
Two pack filler consists of two materials: a ready mixed paste and a hardener/catalyst. These are then mixed together to form the filler.
It is very hardwearing and durable.
For use on interior and exterior surfaces.
Some two pack is coloured to match wood.
It is very quick drying.
Use on wood, metal, stone and plastic.

## Slide 9: Cleaning agents
Sugar soap is the most common cleaning agent used. It is available in three forms:
powder
liquid concentrate
wipes.
It can be used to remove:
dirt, and general surface contamination
oil/grease.

## Slide 10: The washing down process
There are two methods of washing down.
Standard washing down
Washing down to a finish
Washing down ‘to a finish’ is carried out on surfaces that don’t require painting.
Begin washing from the bottom to the top to avoid leaving streaks.
Sugar soap must be rinsed well to avoid defects in the paint finish.
Always follow the manufacturer’s instructions when mixing.

## Slide 11: Caulk
Decorator’s caulk is a flexible filler ideal for gaps where there is movement between two surfaces.
Available in three different colours:
Magnolia
Brown
White
It cannot be rubbed down, so care must be taken not to over-apply it to a surface.

## Slide 12: Shellac and white knotting
Knotting can be the traditional brown variety or white (bleached).
Used to seal knots in bare wood to stop the resin from bleeding through.
Knotting is spirit-based, which means brushes must be washed out in methylated spirits.

## Slide 13
Any questions?