## Slide 1: PowerPoint 7: Access equipment
PowerPoint presentation
Unit 110: Decorative finishing and industrial painting occupations

## Slide 2: Types of ladders
There are two main types of ladders.
Pole (leaning) ladders: Consisting of one section, often used on scaffolding, normally made from one piece of wood split down the middle, hence the name ‘pole’.
Extension ladders: Consisting of two or more separate sections of ladder. These ladders are used to access areas for a short duration that stepladders cannot reach. Made of aluminium, fibreglass or wood.

## Slide 3: Types of ladders
Fibreglass Pole Aluminium

## Slide 4: Telescopic ladders
Another popular choice of ladder is the telescopic ladder which has the advantages of being lightweight, portable and easily stored.

## Slide 5: Stepladders
      Stepladders are used for low level work. They are made of two types of
      material.
      Aluminium
      Fibreglass

## Slide 6: Hop ups
Like stepladders, hop ups are intended for low level work
They are made from aluminium or a combination of aluminium and fibreglass

## Slide 7: Podium steps
Podium steps, like hop ups and stepladders, are used for low level work but have an enclosed working platform which greatly reduces the risk of falls from height. They are made from aluminium or a combination of aluminium and fiberglass.

## Slide 8: Inspecting access equipment
it is a requirement under various H&S regulations to carry out regular inspections of equipment.
These inspections will help prevent:
slips, trips and falls of the operative
cuts and abrasions when handling the equipment
materials and tools falling from the equipment.

## Slide 9: What you should check
Cleanliness of the equipment
Suitability of the equipment of the task
Working parts function correctly
If the equipment has previously been repaired
If previous damage has been covered up ( e.g. painted over)
If there are any missing, loose, cracked, rotten, buckled or broken components
If the equipment is manufactured to current safety standards

## Slide 10: Inspection time periods
There is no set time period for most access equipment to be inspected. However, it should be inspected:
before use
during use (daily)
after use
after adverse weather conditions
following an accident which may have involved the equipment
in accordance with current health and safety regulations.

## Slide 11: Tagging systems
Many companies have a system for the inspection and maintenance of equipment. You may see an inspection tag fixed to access equipment stating when the inspections were carried out and by who.

## Slide 12: If faulty or damaged equipment is discovered
Put it aside, tell others and mark it clearly ‘FAULTY, DO NOT USE’
Report it to your supervisor as soon as possible.
Never assume equipment is safe just because someone says so and never feel obliged to use equipment that you do not feel is safe.

## Slide 13
Any questions?