## Slide 1: PowerPoint 9: Paint application tools
PowerPoint presentation
Unit 110: Decorative finishing and industrial painting occupations

## Slide 2: Paint brushes
It is important to understand what choices of brushes are available as there are many types.
The brush you select should be:
suitable for the task
comfortable in the hand
suitable for the type of paint being used
durable enough for frequent cleaning and re-use.

## Slide 3: Components of a paint brush
Handle – made from plastic resin, or hardwood . Often sealed with a lacquer to protect it.
Filling – usually natural bristle or synthetic filaments.
Ferrule – a metal band that holds the filling and the handle together.
Setting – a water- and solvent-resistant resin which bonds the fibres of the filling together, and into the handle/stock.
Spacer – small wood, plastic or cardboard strips that create ‘spaces’ in the filling to act as a ‘reservoir’ to hold paint.

## Slide 4: Paint brush components
All brushes are made up of five parts.
Ferrule/stock
Handle
Epoxy/setting
Spacer
Filament/filling
The parts of a brush

## Slide 5: Types of paint brush filling
There are three types of filling for the types of paint brushes commonly used:
Pure bristle: Mostly suitable for oil-based paints but larger brushes may be suitable for water-based paints too.
Synthetic filament: Man-made filling, mostly for use with water-based paint, but some are used with oil-based paints.
Mixed: Some brushes contain a mixture of natural and synthetic filling.
How brushes and rollers are made: https://youtu.be/cThURAhuRb4

## Slide 6: Pure bristle
Advantages:
Wears naturally
Resistant to most chemicals, strong and durable
Holds a lot of paint.
Disadvantages:
Poor performance with some water-based paints
Can take a while to form into shape.

## Slide 7: Characteristics of natural bristle
Natural bristles naturally taper and have a split end. This split end helps reduce brush marking.

## Slide 8: Synthetic filament
Advantages:
Resistant to chemicals
Hold their shape when wet, longer lasting
Finer finish in water-based coatings.
Disadvantages:
Filaments can break, bend or become misshapen
Some types do not perform well in oil-based paint.

## Slide 9: Tips when using brushes
Dampen the bristles/filaments slightly before use to allow the paint to be drawn into the filling quicker and help prevent a dry build up near the ferrule.
Don’t overload a brush, if you have to twist the brush around after you have dipped, you have too much paint on it.
Spin out access paint before washing the brush out.
Once washed, spin out access water/brush cleaner/thinners.
Leave the brush flat or suspended on a hook in a dry vented area.

## Slide 10: Paint rollers
The selection of roller sleeve and frames will depend on the type of paint being applied and the surface it is used on.
Roller sleeves normally come in four common pile depths:
Short: for finishing paints.
Medium: for emulsions, water-borne eggshells, masonry paints to smooth walls and ceilings.
Long: for emulsions and /or masonry paints to large broadwall areas with a textured surface.
Extra long: For deep textured surfaces like dashing.

## Slide 11: Tips when using rollers
Always wash brand new roller sleeves out before use to prevent loose fibres and pile contaminating the paint and ending up in the dried paint coating.
Dampen sleeves slightly before use to allow paint to be absorbed into the pile quicker.
Scrape out access paint back into the container before washing out.
Spin the roller out after you have washed it.
Always leave the sleeve standing upright or suspended in a dry environment to avoid flattening the pile.

## Slide 12: Types of roller sleeve
Sheepskin Woven polyamide Microfibre
Mohair Foam Knitted polyester

## Slide 13: Frame types and sizes
There are three common types of roller frame:
Single arm (yoke) cage type frames
Double arm frames (some adjustable)
Radiator roller frames
Cage frames come in two widths of 175mm and 225mm
Double arm frames come in 300mm 375mm 450mm and 600mm
Radiator arms/frames take roller sleeves between 75mm and 100mm

## Slide 14: Types of roller frames
Cage frame Adjustable double arm frame
Radiator roller frame Double arm frame

## Slide 15: Paint kettle/pot
Description: A plastic or metal pot with a handle to hold paint.
Uses: Should always be used instead of the actual paint tin itself as it is lighter, holds less paint in case of a spill and avoids fluff and dust getting in and contaminating the paint.
Sizes Most paint kettles will hold approx 2.5 litres of paint, but it is best practice to only pour out the amount you actually need.

## Slide 16: Roller trays and scuttles
Trays: Used to hold small amounts of paint (up to 2.5 litres).
Scuttles: Hold larger amounts of paint up to 15 litres.

## Slide 17
Any questions?