## Slide 1: PowerPoint 5: Sustainability of resources
PowerPoint presentation
Unit 110: Decorative finishing and industrial painting occupations

## Slide 2: Sustainability and the decorating industry
SUSTAINABILITY: ‘avoidance of the depletion of natural resources in order to maintain an ecological balance’.
Put simply, the more we use products from unsustainable sources, the quicker they will run out.
The less we have, the more expensive they will become.
REDUCE!...RE-USE!...RECYCLE!

## Slide 3: The difference you can make
Cut down on waste
Store products correctly
Dispose of waste materials correctly
Use water-based products, not oil based
Recycle and re-use packaging whenever possible
Use electronic messages instead of notes on paper
Look after tools and equipment so they don't have to be replaced so often.

## Slide 4: Volatile Organic Compounds
    Or VOCs, are harmful chemicals that are released into the air and contribute to pollution and global warming.
    All manufacturers (of paints, stains, varnishes, solvents, etc.) have now reduced the amount of volatile organic compounds, the solvents, used in their products.
    The lower the VOC content, the less of an impact on the environment
    By 2010, all paint and varnish coatings became ‘VOC compliant’.
https://youtu.be/MlAIO4MiXRU

## Slide 5: The five VOC categories
VERY HIGH…..VOC content higher than 50%
HIGH…..............VOC content 25% to 50%
MEDIUM….......VOC content 8% to 24%
LOW…..............VOC content 0.30% to 7.99%
MINIMAL…......VOC content 0% TO .29%
Explanation of VOCs https://youtu.be/gUdbPpcS7ew

## Slide 6: VOC labelling

## Slide 7: Non-toxic paints
    Some companies now produce materials that are completely non-toxic, environmentally safe products with practically zero VOC content.

## Slide 8: Waste disposal
Care must be taken when disposing of hazardous waste. Paint coatings can be classed as hazardous.
Try not to order more materials than you need for a job.
Don't pour excess materials or waste from cleaning processes into a sink or into a drain.
Wipe out containers and dispose of with normal household waste.
Check with your local authority and manufacturer’s instructions for guidance on how to dispose of hazardous materials.
Look at the following video for more information: https://youtu.be/d8l9FFLyjJU

## Slide 9: Brush and roller cleaners
An environmentally friendly alternative to traditional brush cleaning

## Slide 10
Any questions?