## Slide 1: PowerPoint 11: Paint materials
PowerPoint presentation
Unit 110: Decorative finishing and industrial painting occupations

## Slide 2: Types of paint
There are two common types of paint:
Water-based coatings are those where the binder is dispersed in the water.
Solvent/oil-based coatings are those where the binder is dissolved in a solvent.

## Slide 3: Common water-based paints
There are many types of water-based paints for use on ceilings, walls and interior or exterior woodwork.
Primer – often the first coat in a paint system
Undercoat – an intermediate coating
Gloss – a finishing coat on wood and metal trim
Satin – a finishing coat for ceilings, walls and trim
Eggshell – a finishing coat for ceilings, walls and trim
Emulsion – a finishing coat for ceilings and walls

## Slide 4: Common oil/solvent-based paints
Oil or solvent-based paints are also used in a similar way to their water-based equivalents:
Gloss
Undercoat
Primer
Satin
Eggshell

## Slide 5: Water-based paints: new technology
As you may have noticed, oil-based coatings have water-based alternatives.
Water-based coatings have less of an impact on the environment.
Water-based coating have a lower VOC content and are generally considered more sustainable.
Many countries have banned oil-based paints completely.
Millions of pounds have been spent on their development.
There are advantages and disadvantages to both types.

## Slide 6: Water-based paints
ADVANTAGES:
Quick drying
Low odour/sustainable / kinder to the environment
Non/slower yellowing
DISADVANTAGES:
Often not as durable as oil-based
Brush marks don't flow out due to the paint drying too quickly
Sheen level is not as deep compared to oil-based gloss

## Slide 7: Oil-based paints
ADVANTAGES:
The paint film is often harder and more durable
Brush marks flow out
Deep sheen compared to water based gloss
DISADVANTAGES:
Slow drying
Yellowing/discoloration of the paint film
Strong odour/not sustainable, less kind to the environment

## Slide 8: The five sheen levels of paint
    How shiny a paint is, or the ‘sheen level’ depends on the type and ratio of the ingredients in the paint.
    Matt LOW SHEEN
    Eggshell
    Silk
    Satin
    Gloss HIGH SHEEN

## Slide 9: Emulsion
A common water-based paint, used on ceilings and walls.
There are three sheen levels:
Matt
Mid/soft sheen
Silk
The higher the sheen level, the easier the surface is to wipe clean.
Applied by brush, roller or spray.

## Slide 10: Contract matt emulsion
A cheaper type of emulsion which is ideal for new plaster as it is permeable. This means it allows any moisture in the surface to escape.
It is often used on new buildings, or where a cheaper alternative to vinyl emulsion is required.
It is not suitable for ‘high traffic’ areas or areas that need wiping/cleaning.

## Slide 11: Oil and water-based primers
For use under undercoat or other finishing paints.
Not all primers are the same. There are separate types for:
Wood
Metal
Plastic
Tiled or glazed surfaces
Primers are part of what is known as a paint system and the first coating on a bare surface.

## Slide 12: Some common primers
Acrylic primer: for hard and soft wood, quick drying, low odour, does not seal knots, not always suitable for exteriors.
Aluminium wood primer: for hard and soft wood, excellent adhesion, seals knots, slow drying, dark grey in colour.
Metal primer: various types depending on the type of metal.
Universal primer: for wood and metal surfaces.
Specialist primers: for difficult surfaces such as ceramics, Formica, melamine and plastic.

## Slide 13: Oil and water-based undercoat
Undercoat is normally much thicker than gloss and is not intended as a finishing paint.
The purpose of an undercoat is to:
hide the existing colour of a surface
provide a smooth and sold base for a top coat
adhere to the surface of previous coatings.
It can be applied by brush roller or spray. It is mostly used on wood and metal work.

## Slide 14: Water and oil-based satin and eggshell
These are classed as ‘finishing paints’, the final coat applied to a surface.
They can both be used on:
ceilings
walls
woodwork
metal work.
They are considered durable and because of the smooth finish they are wipeable.

## Slide 15: Oil and water-based gloss
Gloss is a finishing paint, which can be used on interior and exterior tasks.
Gloss can be applied to:
woodwork
metal work
walls.
Like eggshell and satin, gloss can be easily wiped clean, making it a good choice for surfaces that require a lot of maintenance.

## Slide 16: Varnishes
Varnishes are clear or translucent coatings designed to enhance and protect natural wood. They can be used internally or externally.
Varnishes can be oil or water based and come in four finishes:
matt
eggshell
satin
gloss.
The sheen level of varnish depends of the ratio of the ingredients.

## Slide 17: How paint is made
Watch the following video to see how paint is made:
www.youtube.com/watch?v=f39o4EVqx9U

## Slide 18
Any questions?