## Slide 1: PowerPoint 8: Painting tools and equipment
PowerPoint presentation
Unit 110: Decorative finishing and industrial painting occupations

## Slide 2: Stripping knife / scraper
Description: Stripping knives have stiff blades. The best quality knives have hardwood handles.
Uses: Removing wallpaper, loose and flaking paint nibs and other surface defects.
Sizes: 25mm 50mm 75mm 100mm

## Slide 3: Filling knives/blades
Description: Filling knives/blades have thin flexible blades to help apply filler. The best quality blades can bend through 90 degrees and spring back into shape.
Uses: Applying various filling materials.
Sizes: 25mm 50mm 75mm 100mm

## Slide 4: Dusting brushes
    Description: Similar to a paint brush with either pure bristle, or synthetic (manmade) filaments.
    Uses: An important piece of equipment to remove dust and general debris from a surface before painting.
    Sizes: Normally 75mm or (100mm)

## Slide 5: Hammer and nail punches
Description: Nail punches are made from hardened metal to be able to withstand blows from a hammer.
Uses: Used with a hammer to tap protruding nail heads back below the surface.
Sizes: 1.6mm, 2.4mm, 3.2mm, 4mm and 4.8mm

## Slide 6: Shave hooks
Description: Not actually a hook, but a blade on a metal stem.
Uses: Mostly used in the removal of paint coatings by heat or paint stripper.
Types: Combination to access flat areas and mouldings. Triangular for flat surfaces only
Triangular Combination

## Slide 7: Skeleton/caulking gun
Description: A handheld tool which holds tubes of decorator’s caulk, silicone and other flexible sealants
Uses: To apply flexible fillers and sealants into cracks and gaps in skirting boards, architraves, coving and cornices.
Types: Best quality skeleton/caulk guns are made of metal, Some are battery operated.
Sizes: Two sizes, to accept 310 or 380ml tubes.

## Slide 8: Sanding blocks
Description: Rectangular blocks which can be made for the task or cut from a piece of wood.
Uses: To assist the decorator abrading a surface. The use of blocks can help produce a flatter surface quicker and using less effort.
Types: Rubber, cork, or wood.

## Slide 9: Power tools
Power tools can often make a task easier and quicker.
The main hazard with power tools, which will be identified in a risk assessment is an electric shock, which can be fatal.
The reduce the impact of an electric shock all equipment should be 110 volt and tested as required.
A transformer will be required to reduce the voltage from 240 volts to 110.
All 110 volt equipment is coloured yellow and has different connections to 240 volt.

## Slide 10: 110 volt equipment

## Slide 11: Hot air heat gun
A modern alternative to cartridge gas torches.
Advantages:
less likely to cause a fire
less likely to scorch the wood
Disadvantages:
requires an electrical supply
slower than gas

## Slide 12: Powered abrading equipment
Mechanical abrading is becoming popular with the introduction of ‘dust free’ abrading which uses special abrasive pads.
These modern sanding units have a built-in vacuum unit, which lifts dust from the surface.

## Slide 13: Power sanding extension

## Slide 14: Other useful items
Stanley knife for general use
Filling board to put mixed filler on
Buckets for holding water/rubbish
Sponges for use when washing down
Rags for wiping paint spots before they dry
Pliers/pincers to remove nails, pins, clips etc.
Screwdrivers: a selection of flat and Phillips heads

## Slide 15
Any questions?