## Slide 1: PowerPoint 3: Reasons for decorating
PowerPoint presentation
Unit 110: Decorative finishing and industrial painting occupations

## Slide 2: Why decorate?
There are four reasons for painting and decorating. They are:
decoration
identification
preservation
sanitation.

## Slide 3: Decoration
This is probably the most common reason – to improve the look and appearance of a surface or area.
Certain colours can change the ‘feel’ of an area.
Colour schemes give the impression of warmth, coolness and space.
Certain colours can improve our mental health and wellbeing.
Redecorating will improve a tired and shabby area.
People may just ‘fancy a change’.

## Slide 4: Identification
We associate colours with certain objects. For some fire extinguishers and situations, red often means ‘danger’ or ‘stop’ etc.
The contents of fire extinguishers are easily identified by a colour.
In industrial environments the contents of some pipes are identified by colours.
Gas | RAL 1004
Fire fighting | RAL 3000
Air | RAL 5012
Combustible liquids | RAL 8001
Acids and alkalis | RAL 4001
Water | RAL 6010
Other liquids | RAL 9005
Steam | RAL 9006
Pipe contents
RAL code
Notes: Linked to worksheet 3

## Slide 5: Preservation
    One of the most important reasons for decoration. If a surface is not preserved it will not last long, especially outside.
    Wood – will rot when exposed to moisture.
    Metal – corrodes due to moisture, acid rain etc.
    Render – becomes dusty and friable due to extreme weather.

## Slide 6: Sanitation
A surface that is porous or rough is hard to clean. This means germs and bacteria will survive on its surface.
Non-porous smooth durable paint will mean a surface can be frequently and easily cleaned.
There are also some paints that are made with special ingredients to combat mould and bacteria.

## Slide 7: Summary
The reason a surface is decorated will often depend on the surface and the environment it is in.
The priority for painting depends on the circumstances.
An exterior wooden window will need preserving.
An interior wall in a kitchen needs to be washable.
The walls of a study should be a calm colour.
The colour of a gas pipe needs to be yellow.

## Slide 8
Any questions?