## Slide 1: PowerPoint 6: Materials to protect surrounding areas
PowerPoint presentation
Unit 110: Decorative finishing and industrial painting occupations

## Slide 2: Why the working area should be protected
The outcome of not protecting the working area can be:
unnecessary disagreements with customers or clients
increased insurance premiums
loss of future business
costly insurance claims
loss of reputation.

## Slide 3: Items that may need protecting
Flooring
Electrical items
Furniture, fireplaces
Mirrors, pictures, wall art
Lighting/light fittings, shades, lamps.
Ceiling fans, air-conditioning vents, ducts
Conservatories, plants, furniture, windows, decking
Blinds, curtains, windows, screens, vents, sockets switches

## Slide 4: Types of protection
Each item type which needs protection will determine the material or materials to be used.
Selecting and using the wrong type of protection could result in damage, which will have to be put right at your expense.
The three ways of protecting property:
Masking
Sheeting
Removal

## Slide 5: Cotton dust sheets
The quality of cotton dust sheets can vary.
Types: Light and heavy duty (can be rubber/polythene backed)
Uses: Covering floors, furniture, stairs, paths, gardens, etc.
Sizes: 7.2 m x 0.9m 3.6 m x 2.7m 3.6 m x 3.6m
Advantages: Durable, cover large areas, reusable, long-lasting
Disadvantages: Paint/fluids can leak through some sheets; they need frequent washing/cleaning.

## Slide 6: Plastic sheeting
Plastic sheeting is a cheaper alternative to cotton dust sheets
Types: Clear thin polythene sheeting. Some types have self-adhesive edges
Uses: Ideal for covering furniture and electrical items
Sizes: 3.6 m x 2.7m 3.6 m x 3.6m
Advantages: Lightweight, cheap, water/dustproof.
Disadvantages: Easily torn, not durable, need taping down, single use.

## Slide 7: Heavy duty polythene (also known as tarpaulin)
A stronger, more durable type of sheeting
Types: Heavyweight waterproof PVC polyethylene often reinforced with a nylon mesh
Uses: Same use as cotton dust sheets
Sizes: 6 m x 4m 10m x 8m,
Advantages: Large size, waterproof, durable, reusable, can be tied to a structure if required, does not rot.
Disadvantages: Can be difficult to handle, slippery on some floors.

## Slide 8: Masking tape
There are many different types of masking tape. It is important to select the correct type for the work.
Types: Low tack , standard crepe, exterior, 7-day, painter’s tape, PVC
Uses: Interior or exterior depending on the type
Sizes: 25mm, 50mm, 75mm, 100mm
Advantages: Wide selection of types
Disadvantages: Can be costly to buy good quality tapes; incorrect use can damage paint surface; single use; paint can creep under it.

## Slide 9: Some types of masking tape

## Slide 10: Sheet materials
Boarding, although more expensive, is ideal for protecting large flat areas.
Types: Hardboard, plywood, MDF, reinforced PVC, heavy duty cardboard, Correx
Uses: Interior floors or exterior ground areas
Sizes: Typically 2400mm x 1200mm
Advantages: Durable, impact resistant, non-slip, non-absorbent, reusable.
Disadvantages: May be too large for some areas.

## Slide 11: Brown masking paper
A plain brown paper, sold in rolls of various sizes, sometimes with a self-adhesive edge
Advantages: Cheap, easy to apply, can fit around curved surfaces, low tack so it does not damage surfaces when removed.
Disadvantages: Single use, not waterproof, easily torn or damaged, low adhesion can also be a disadvantage.

## Slide 12: Masking machines
Used with brown masking paper. These machines can speed up the masking process
Floor masking machine Hand-held masking machine

## Slide 13: Polythene self-adhesive masking film
A translucent, thin plastic sheet on a roll, with a self-adhesive edge, which can be unfolded into a larger size.
Advantages: Waterproof, easy to apply, expandable, will emit light (suitable for windows), various size rolls.
Disadvantages: Single use.

## Slide 14
Any questions?