## Slide 1: PowerPoint 7: Install roofing backgrounds and ancillary components
PowerPoint presentation 1.1
Unit 101: Introduction to the Built Environment
Unit 111: Roofing occupations

## Slide 2: Fire-stopping
Roofs should be constructed to offer adequate resistance to the spread of fire.
The junction between a separating or compartment wall and a roof should be fire-stopped. If there are gaps, then fire, smoke and flame can spread from one compartment to the next across the wall.

## Slide 3: Fire-stopping
A soft fire-resistant packing, such as mineral wool, should be used to allow for movement in roof timbers and prevent ‘hogging’ of the tiles.
A cavity barrier should be provided within boxed eaves. The cavity barrier should be a wire-reinforced mineral wool blanket, at least 50mm thick, nailed to the rafter and carefully cut to shape to fully seal the boxed eaves.

## Slide 4: Ventilation at the eaves
Roof voids must be ventilated in order to stop warm air condensing on cold surfaces. Condensation encourages rot and mould growth.
Eaves ventilation is important as it creates an airflow through the lower section of the loft and can help to prevent condensation. Sometimes this airflow is blocked with excess insulation.
It is important to insulate correctly but also to add vents in the right places. This allows the roof to breathe but keeps the home warm.

## Slide 5: Warm or cold?
Flat roofs are generally classed as ‘Cold’ or ‘Warm’ and it depends on the position of the insulation. Here are two videos to explain the difference:
  Cold flat roof
  Warm flat roof

## Slide 6: Air flow recommendations
Ventilation recommendations will depend on the following:
Warm or cold roof
Pitch degree

## Slide 7: Fascia boards
The top of the fascia board should be at a height to support the eaves course of tiles at the same pitch as the rest of the roof. If the fascia is too high the eaves tiles will tilt up, or 'sprocket', if too low then they will dip. Neither is advisable.
For every design of tile, every degree of rafter pitch, with or without over fascia ventilation, the height of the fascia board above the rafter, or counterbatten, will be different.
Some manufacturers provide tables of fascia board heights for their products – if not, you will have to work it out manually.
The size and shape of an over fascia ventilation grill will also affect the fascia board height.

## Slide 8: Underlay
You need to be familiar with the different ways to set out the underlay in each of these areas:
eaves/openings/abutments
hips
ridges
valleys.

## Slide 9: Recommendations
BS 5534: How does it affect the way roofing contractors work?
BS 5534 provides the construction industry with guidance on best practice on the installation of a slate or tiled roof. It contains a vast array of information, ranging from batten selection and fixing methods to wind uplift formulas, providing manufacturers with a means of calculating fixing specifications.
It is not a legal requirement to install a roof in accordance with the British standard. However, the standard can be included within a specification, and this can be upheld in a court if necessary.

## Slide 10: Recommendations
Manufacturers will also provide recommendations on how to set out underlay, minimum requirements for laps and upstands and the types of sealing or taping to use.
Manufacturer recommendations include:
minimum lap requirements for felting a roof
upstand heights of felt to abutments
sealing/taping recommendations.

## Slide 11
Any questions?