## Slide 1: PowerPoint 8: Dry fix
PowerPoint presentation 1.1
Unit 101: Introduction to the Built Environment
Unit 111: Roofing occupations

## Slide 2: Bedded ridge tiles
Changes in BS 5534 means that the use of mortar only to fix roof tiles is now deemed as insufficient. Not only should careful consideration be given to the correct mix of sand and cement but tiles bedded with mortar must also be accompanied by a mechanical fix.
The most important thing to remember is to get the mortar consistency and strength right. The mortar must be firm enough to support the tile but wet enough to be workable.
Recommendations are that the roofing mortar is 1:3 cement: sand with plasticiser (other options are also available.). The mix should be based on sharp sand and the bedding should be completed in one operation.

## Slide 3: Bedded ridge tiles
Watch this video from a manufacturer and make notes on what fixings were used.
What fixings were used?
Ridge brackets, nails, stainless steel screws, dentil slips, plastic clamps.

## Slide 4: Other methods
Other methods can include packing – this involves placing materials into the bedding area under the ridge tiles themselves.
Why are additional fixings needed? Why is mortar not enough anymore?
Increase in extreme weather such as gale force winds.
Mortar alone can move and crack, meaning repairs and repointing will be needed more frequently.

## Slide 5: Dry ridges
Avoiding mortar bedding, with the associated risks and extra maintenance, is becoming ‘best practice’.
Manufacturers are supplying a more extensive range of dry fix solutions, which are mortar- and maintenance-free (BS 5534 compliant), and are also able to contribute to ventilation requirements.

## Slide 6
Any questions?