## Slide 1: PowerPoint 5: Double-lap roof coverings
PowerPoint presentation 1.1
Unit 101: Introduction to the Built Environment
Unit 111: Roofing occupations

## Slide 2: Plain tiles
Plain tiles have been available in one form or another for hundreds of years.
They are traditional, small, rectangular tiles: either clay or concrete.
They are smaller in size than other tile/slate types and generally are used for small works, such as porches, bays and vertical tiling.
Standard fittings include under-eaves and tops tiles which create a double course at the bottom and top edge.
Tile-and-a-half are used to create a half bond on every other course.
Variations are available for hips, valleys and vertical areas.

## Slide 3: Plain tiles
What is the minimum roof pitch for plain tiles?
35°
Are plain tiles single or double lap?
Double-lap
Which is heavier: clay or concrete?
Concrete
What is the standard size of a plain tile?
265 x 165mm

## Slide 4: Tools and materials
Materials for roofing include the following and cross over into various other jobs.
Sand and cement for mortar
Plain tiles
Eaves
Tile-and-a-half
Softwood battens
Nails

## Slide 5: Tools and materials
Using reclaimed tiles is becoming increasingly popular for several reasons. For example, they can help a client who needs a repair or wishes to extend an existing property. Reclaimed tiles:
can be used to match existing ones
retain a period feel
offer a weathered look
are cheaper than new
are environmentally friendly.

## Slide 6: Plain tiles
What is the recommended standard size for the batten when using plain tiles?
38mm x 25mm
Discuss the process for establishing first course and eaves batten position.

## Slide 7: Plain tiles
Once you have your fixed first point you can set out the other battens to the maximum gauge length and make any adjustments required in the last metre or so before you reach the ridge.

## Slide 8
Any questions?