## Slide 1: PowerPoint 6: Natural roof slates
PowerPoint presentation 1.1
Unit 101: Introduction to the Built Environment
Unit 111: Roofing occupations

## Slide 2: Use of slate
Slate has lined our roofs since Roman times.
Slates can be local, imported and even man-made.
Slates are durable, hard-wearing and watertight.
Welsh slate is universally recognised as the highest quality slate available; however Spain is the largest exporter.
Slate roofs are not cheap – good quality reclaimed slate is in high demand and offers a cost-effective and sustainable solution.

## Slide 3: Natural slate
The most common size for slate is 500mm x 250mm.
Slates have a face, bed, head and tail.
Pre-holed slates will come in different sizes to accommodate different roof pitches.
The amount of headlap will depend on the pitch and the location as the exposure to wind and rain needs to be taken into account.
Natural slates are double lap.

## Slide 4: Tools and resources
There are certain tools specifically designed to use with slate:
Slater’s hammer
Slate knife
Break iron
Holing machine
Slate cutters

## Slide 5: Tools and resources
Slater’s hammer – sometimes called a pick hammer. This is a traditional hammer with a small head for accuracy and pick used to make holes.
Break iron and slate knife – used together to cut slates; the break iron works as an anvil.
Holing machine – traditionally it would have been the apprentice’s job to hole all the slates for the craftsman.

## Slide 6: Tools and resources
There are certain materials to use for slating, outlined within the BS 5534 standards.
What size should the battens be?
50mm x 25mm softwood
What other materials are needed for natural slate roofing?
Natural slates
Nails specific for slating
Slate hooks

## Slide 7: Gauge
How do you work out the gauge for natural slates?
Take the minimum headlap away from the full length of the slate then halve
Gauge = length – headlap divide by 2
Traditionally British slates have always been supplied in imperial and had a default headlap of 3”. The maths was simple: 18” slate minus 3” to give you 15”, half of which is 7½”. All slate gauges worked out to a full or half inch.
Slates nowadays are in round metric measurements, such as 350mm, 400mm, 500mm, and most are pre-holed so you will need to know the headlap to work out the right gauge.
Notes: Use diagrams

## Slide 8: Gauge
The gauge for natural slates
This is based on the formula:
Length – headlap = gauge
2
For example:
400mm – 70mm
2 = 165mm
Notes: Use diagrams

## Slide 9: Grading and sorting
Slates need grading. This is a very important part of the job.
What are they graded on?
Thickness.
What are the three categories of grading?
Thick, medium and thin.
Where would each grade go on the roof?
Thick at the bottom, medium in the middle and thin at the top. Broken or damaged slates found during sorting should be saved for under eaves courses and to use as half slates/raking (angle) cuts.

## Slide 10: Grading and sorting
What problems could occur if the slates are not graded and sorted before fixing?
Roof will not sit flat due to variants in thickness.
Leaves the roof vulnerable to wind and driving rain.
Does not look good as not even and the slates do not sit well together.
How to sort and grade
Inspect and separate
Weight
Storing requirements

## Slide 11: Holing position
Not all slates are pre-holed. The holing point should be marked on the reverse of the slate (bed).
To establish the holing point use the formula:
Holing point = gauge + headlap + 6 to 12mm
6 to 12mm explanation: When smaller battens were used, 6mm clearance was enough, using the correct, larger batten (50x25mm) and for metric measurements the norm seems to be 10mm.

## Slide 12: Holing position
Holing position
Gauge + headlap + 6–12mm
20–25mm for the edge
X
Holing position
Notes: Use diagrams

## Slide 13: At the eaves
How can you work out the position of the under-eaves and first course battens?
How much should the overhang into the gutter be?
Overhang of 50mm.
First course batten positioned so the top of the slate sits halfway onto the batten and 50mm into the gutter.
Under-eaves batten set one gauge down.
Additional batten at under eaves.

## Slide 14: At the eaves
Official guidance from BS 5534 for the eaves:
A double course of slates should be used.
The under-eaves slates should be of a length equal to the sum of the gauge and headlap of the full slates.
The under-eaves slates should be laid face down and head-nailed to the eaves batten or an extra batten.
The under-eaves slates should be overlapped with a full slate with the joints located notionally over the centre of the under-eaves slates.
Full-size slates should not be laid sideways to form the under-eaves course.

## Slide 15
Any questions?