## Slide 1: PowerPoint 1: Safe working
PowerPoint presentation 1.1
Unit 101: Introduction to the Built Environment
Unit 111: Roofing occupations

## Slide 2: Statistics
Top five safety risks – in order of how many workers have died:
Falling from height – fall from a ladder
Falling from height – fall through a fragile roof
Lifting operations
Struck by plant
Overturning plant

## Slide 3: Reporting
One of your responsibilities under HASAWA is to deal with or report hazards in the workplace.
Why is it important for hazards to be reported?
Prevent danger to others
Prevent accidents
Correct dangerous situations
How can this be done?
Hazard book/Near miss register

## Slide 4: Changing circumstances
Hazards are common on construction sites: they are busy places, constantly changing and going through new stages of development as construction is carried out. As each stage begins, a whole new set of potential hazards need to be considered.
Extreme weather conditions, such as heavy rain, strong winds or extreme temperatures, can make construction sites even more hazardous.

## Slide 5: Changing circumstances
Heavy rain – long periods of rain can cause trenches to fill with water, leading to flooding of areas; smooth surfaces can become slippery.
Wind – strong winds prevent working at height; scaffolding can become unstable; unsecured roof materials may come loose; sand/cement may be blown across site.
Heat – may change the behaviour of materials (setting quicker, melting) and cause dehydration, sunburn and heat exhaustion.
Snow – can add enormous weight to roofs and other structures; can cause collapse of structures; make surfaces slippery; block access; affect behaviour of materials.

## Slide 6: Correct storage
What is a combustible substance?
It is material which can be either flammable or explosive, or both, such as paint, cleaning agents etc.
HSE has some basic advice on how to store such materials correctly.
Exchange – in many cases it can be possible to find and use an alternative material which is less dangerous; this option should always be first considered first.
Ignition – keep materials away from any spark or flame that could trigger the vapours.

## Slide 7: Correct storage
Containment – the materials should be kept in proper containers with lids.
Ventilation – the area should be well ventilated to disperse any vapours that could trigger off an explosion.
Separation – always keep flammable substances away from general work areas.
Certain materials such as LPG (liquefied petroleum gas) need to be housed in specially built storage areas.

## Slide 8: Chemicals
COSHH is Control of Substances Hazardous to Health, 2002.
These are the new international style symbols, which came into effect in June 2015.
Any chemical will have the corresponding symbol/s displayed along with storage advice on the safety data sheet.
Chemicals need to be stored in line with COSHH requirements.

## Slide 9: Chemicals
How should each be stored correctly?
In properly labelled containers
Containers with appropriate securable lids
In locked cupboards
Away from heat sources
Dry places
Off ground level
Correct temperature

## Slide 10: Health and hygiene
It is both your own responsibility, as well as your employer’s, to make sure you stay safe and healthy at work.
The employer will need to provide basic welfare facilities, no matter where you are working and these must follow minimum standards.
Toilets – if there is a lock there is no need to have separate male and female toilets. There should be enough for the site workforce. If there is no running water there must be chemical toilets.
Washing facilities – there should be a wash basin large enough to wash up to the elbow. There should be soap, hot and cold water and, if you are working with dangerous substances, showers are needed too.

## Slide 11: Health and hygiene
Drinking water – clean drinking water should be available, either directly through the mains or supplied as bottled water.
Dry room – this can also operate as a store room; it needs to be secure so that workers can leave their belongings there. It will be used as a place to dry out if employees have been working in wet weather, in which case a heater should also be provided.
Work break area – this is a shelter out of the wind and rain with a kettle, microwave, table and chairs. It should also have heating.

## Slide 12: Noise
The negative health effects of noise include loss of hearing, either permanent or temporary, and tinnitus.
Precautions:
Remove – get rid of the source of noise.
Move – locate noisy equipment away from people.
Enclose – surround noisy equipment e.g. soundproof area or cover with soundproof material.
Isolate – move the workers to protected areas.
Even after all of these are considered, PPE may still be required.

## Slide 13: Noise
How do I know if I need protection?
This is a simple way of carrying out a test to see if a work area is loud enough for action to be taken.
Stand 2 metres away from your mate: you should be able to talk to each other without shouting.

## Slide 14: COSHH
Substances: Lead paint, solvents, adhesives, cement, dust, contaminated soil or water, asbestos etc.
Precautions:
PPE
RPE
LEV
Isolation
Set exposure times
Eye
protection
required
Protective
clothing
required
Foot
protection
required
Protective
gloves
required
Head
protection
required
Notes: Discuss each

## Slide 15: Health risks
Recap – top five: What are the consequences of these health risks?
Exposure to asbestos
Exposure to silica
Manual handling
Exposure to excessive noise
Exposure to excessive vibration

## Slide 16: Health risks: dermatitis
Dermatitis causes your skin to become red, blistered, dry and cracked.
An irritant substance (e.g. mortar) damages and inflames the skin.
It causes unbearable itching and pain.
It occurs when skin is exposed to irritants for a sufficient amount of time.
Wash work clothing regularly and use barrier cream to protect your hands.

## Slide 17: Health risks: asthma
Asthma is not always a condition that you are born with. It can develop over time when you are exposed to certain things (e.g. wood dust).
In your body there are tubes that carry air to the lungs (these are called bronchioles).
The lining of these tubes can become very sensitive: they swell up and restrict the amount of air that can get to the lungs when you suffer from asthma.

## Slide 18: Health risks
Health hazards when cutting clay or concrete tiles with a disc cutter
Silica is a natural mineral present in large amounts in many construction materials, such as concrete roof tiles. The silica is broken into very fine dust (also known as respirable crystalline silica or RCS) during common tasks such as cutting. Regularly breathing in this dust can cause serious lung disease such as silicosis and lung cancer. Recent HSE research has estimated that silica may be responsible for the deaths of over 600 people each year who have worked in construction.

## Slide 19: Risk assessment situations
Cutting roof tiles with a disc cutter
Repointing brickwork on a low wall
Using MEWP
Erecting and dismantling a scaffold tower
Driving a forklift
Mixing mortar

## Slide 20: Risk assessment
Date of risk assessment | Name of person/s:
Identify hazards | 
Identify who is at risk | 
What is the risk from the hazard that may cause an accident? | 
Measures to be taken to reduce the risk | 
Monitor the risk | 

## Slide 21
Any questions?