## Slide 1: PowerPoint 11: Install regular-sized natural slate
PowerPoint presentation 1.1
Unit 101: Introduction to the Built Environment
Unit 111: Roofing occupations

## Slide 2: Bedded verges with slates
Slate widths – min. requirement
Undercloak
Course sequence
Overhang requirement
Bedding and pointing
Fixings – min. requirements
Health and safety procedures

## Slide 3: Slate verges
Official standards: BS 8000-6: Verges
All verge slates should be mechanically fixed in accordance with BS 5534.
Slates should be laid nominal half bond for single size slating, using extra-wide slates where necessary.
A combination of slate widths should be used at verges to enable the bond to be achieved. Slate-and-a-half slates may be used where available. To avoid the risk of thin narrow slates breaking or becoming detached, the combination of slate sizes should not include slates less than 150mm wide.

## Slide 4: Mortar finishes – verges
Official standards: BS 8000-6: Verges
A 100mm wide bed of fully compressed mortar width should be laid onto the undercloak.
Slates should be bedded solidly and edges finished neatly.
The mortar bed should be firm enough to withstand the vibrations of nailing slates or the pressure applied as a result of mechanical fixings.

## Slide 5: Dry verges
Official standards: BS 8000-6: Verges
Dry verge systems should be installed to conform to the manufacturer’s site-work instructions.
Where proprietary dry verge systems are specified, any special verge details recommended by the manufacturer should be used.

## Slide 6: Top edge slates
Slates do not have nibs so they can be finished tight with the top edge.
Two methods

## Slide 7: Top edge slates
How do these two methods help prevent uplift?
Mortar bedded.
Thicker batten supports the heads of top slates and prevents the tails lifting.
What else can be done if the wind resistance needs to be increased?
Two courses of short slates can be provided on double battens to reduce the length of the top course.

## Slide 8
Any questions?