## Slide 1: PowerPoint 10: Install double-lap plain tiles
PowerPoint presentation 1.1
Unit 101: Introduction to the Built Environment
Unit 111: Roofing occupations

## Slide 2: Plain tiles
What is the minimum roof pitch for plain tiles?
35°
Are plain tiles single or double lap?
Double-lap
Which is heavier: clay or concrete?
Concrete
What is the standard size of a plain tile?
265 x 165mm

## Slide 3: Plain tiles at eaves
Formation of eaves receiving hip finishes:
Bedded hip tiles
Bonnet hips
Side-lap requirements
Mitre
Nibs
Arris hips

## Slide 4: Plain tiles at eaves
Formation of eaves receiving valley finishes:
Purpose-made valley tiles
Open valleys

## Slide 5: Plain tiles with valleys
Continuous support provided for ends of tiling battens on each side.
Underlay minimum 600mm wide.
Cut adjacent tiles and tile-and-a-half tiles.

## Slide 6: Verge bedded systems
Types of verge bedded systems used for plain tiles:
flush traditional
undercloak supported
plain tile supported.

## Slide 7: Verges
Different methods for forming a plain tile verge:
Plain tiles and tile-and-a-half alternate course
Overhang requirements
Fixings
Bedding and pointing
Dry fix verge systems
Cloak verge tiles

## Slide 8: Battens
Batten requirements used to receive hip tiles
Batten ends should be:
cut to an angle
fully supported by the hip rafter or noggin
securely nailed
in line on both sides
what about the centre batten?

## Slide 9: Fixings
What fixings are used for bonnet and arris hip tiles?
Mortar bedding – bonnet hip tiles are bedded along the leading edge 50mm wide, arris hip tiles are back bedded.
Each hip tile needs to be nailed into the hip rafter.
The nails to secure bonnet tiles need to be long as the distance down to the rafter and can be as much as 75mm plus the 25mm nail penetration.

## Slide 10: Bedded hip ridge tiles
Another hip system is bedded hip ridge tiles.
How are these secured to plain tiles?
The hip ridge tiles need at least 75mm of coverage on the plain tiles.
Use tile packing within the mortar bedding.
Pointed correctly.

## Slide 11
Any questions?