## Slide 1: PowerPoint 4: Single-lap roof coverings
PowerPoint presentation 1.1
Unit 101: Introduction to the Built Environment
Unit 111: Roofing occupations

## Slide 2: Single-lap coverings
Single-lap coverings definition: ‘a roofing tile which overlaps only the tile in the course immediately below it’.
Single-lap tiles require far fewer units per m² than a double-lap product.
Single lap

## Slide 3: Single-lap coverings to eaves
To position the eaves batten you must measure the underside of the tile, from the bottom of the nib, so you know where the overhang will be positioned and where the tile will be fixed to the batten.
A good guide is to set the first batten so the tail of the eaves course of tiles overhang the fascia just short of the centre of the gutter. This diagram shows the overhang to be 40–45mm.
If there’s no gutter, an overhang of minimum 50mm should be allowed.

## Slide 4: Single-lap coverings to eaves
Once you have the measurement of the tile minus 50mm, you can work out how far up the batten will be fixed.
Secure the batten loosely so you can check the position is correct. The tile should be pulled down squarely onto the batten to ensure the nibs and nail holes are properly located and check the overhang is correct.
Once done, you can secure the eaves batten.

## Slide 5: Single-lap coverings
Once the eaves batten has been secured along the roof, the batten gauge can be worked out according to the size and type of tile, working with an overlap of 75mm.
How is the gauge worked out ?

## Slide 6: Perpendicular lines

## Slide 7: Single-lap coverings to eaves
Other components to be fixed at the eaves are eaves fillers.
What is the purpose of eaves fillers?
The purpose is to close up any gap under the tiles so that birds and vermin cannot enter the roof space.
Notes: Tutor to have examples of eaves filler comb

## Slide 8: Single-lap coverings to eaves
Fixing: It is important that perimeter tiles are all mechanically fixed. Manufacturers will give specific recommendations, as additional nails or clips may be required depending on the pitch and degree of exposure.
Fixing types:
Nails – guidance is given from BS 5534. They should not be less than 3.35mm in diameter and should be able to penetrate at least 15mm into the batten.
Clips – there are tile clips and eaves clips.

## Slide 9: Abutments
Depending on the roof type, you may need to contend with abutments and how you cut the tile will depend on the location.
Top edge abutment – fix the top course tile batten close to the wall, allowing for a minimum 5mm air gap and the nibs of the tiles, then complete the tiling.

## Slide 10: Abutments
Side abutments in general – if possible, the tiling should be set out to fit full standard tiles at left and right-hand abutments.
If it is not possible then tiles must be cut to fit, ensuring that the cut tiles are large enough (at least ½ tile width) to be adequately mechanically secured.
Consider:
cover flashing
secret gutter
minimum gaps
batten position.

## Slide 11: Dry verge systems
UPVC interlocking verge units
Cloaked verge
Continuous dry verge

## Slide 12: Wet bedded verge systems
What is the appropriate setting out procedure for wet fix verge systems?
Minimum 100mm width of mortar
Acceptable overhang
Undercloak
Verge clips

## Slide 13: Cloaked verge tiles
The changes to BS 5534 mean that perimeter roof cladding elements including verges will require a minimum of two fixings, one of which can be a tile clip, adhesive (mortar) or dry verge capping system where appropriate.
Cloaked verge tiles provide a neat finish to the verge.
Other fixing methods for cloaked verge tiles are nails and plug-in face screw and washer and internal clips.

## Slide 14
Any questions?