## Slide 1: PowerPoint 3: Roof structure
PowerPoint presentation 1.1
Unit 101: Introduction to the Built Environment
Unit 111: Roofing occupations

## Slide 2: Roof types
Weather conditions in the UK, with a lot of rain and sometimes snow, mean it makes sense for roofs to be pitched. Pitched means built at an angle. The idea is that rain and snow falls down the angle and off the edge rather than lying on the roof.
Not all roofs are pitched; many extensions and industrial buildings have flat roofs. A problem with a flat roof is that it must be able to support itself as well as any additional weight of snow or rain. A slight angle must be included to allow for the drainage of rainwater. The preferred design of a flat roof fall is 1:40.
Roofs also provide the building with stability by tying the walls together.

## Slide 3: Roof types
Hip roof
Gable roof
Flat roof
Gambrel and valley roof
Gambrel roof
Mansard roof

## Slide 4: Roof features
Rafter – roof rafters are the main structural components of the roof; they are the framework. Rafters rest on supporting walls and are set at an angle for sloped roofs and horizontal for flat roofs.
Wall plate – this is a horizontal timber that is placed at the top of a wall at eaves levels to hold the ends of joists or rafters.
Purlin – this is a beam that supports the mid-span section of rafters.
Bracings – roof rafters need to be braced to make them more rigid and stable and prevent the roof from buckling.
Batten – roof battens are thin strips of wood which provide a fixing point for roof sheets or tiles.

## Slide 5: Roof features
The ridge – top of the roof junction; it is the peak where the rafters meet.
The apex – highest point of the roof, usually the ridge line.
Tiles/slates – roof covering fixed to the battens.
Flashings – used wherever there is a joint or angle to waterproof the roof.

## Slide 6: Roof features

## Slide 7: Roof features
Eaves – area at the foot of rafters. Can be flush so not always visible.
Bargeboard - ornamental feature fixed to the gable end to hide the ends of roof timbers.
Soffits – these are the lower part or overhanging part of the eaves; the underside of the eaves. A flat section of timber or plastic is fixed to the soffit to make it watertight.
Fascia – horizontal, decorative board, wood or PVC, fixed to the ends of rafters at eaves level.

## Slide 8
Any questions?