## Slide 1: PowerPoint 2: Working at height
PowerPoint presentation 1.1
Unit 101: Introduction to the Built Environment
Unit 111: Roofing occupations

## Slide 2: Working at height
Which legislation relates to working at heights?
The Work at Height Regulations, 2005 (WAHR)
There is a simple hierarchy for managing and selecting equipment for work at height. Duty holders must:
Avoid work at height where they can
Use work equipment or other measures to prevent falls where they cannot avoid working at height and
Where they cannot eliminate the risk of a fall, use work equipment or other measures to minimise the distance and consequences of a fall should one occur.

## Slide 3: Collective and personal protection
Always consider measures that protect everyone who is at risk (collective protection) before measures that protect only the individual (personal protection).
Collective protection is equipment that does not require the person working at height to act to be effective, for example a permanent or temporary guard rail.
Personal protection is equipment that requires the individual to act to be effective. An example is putting on a safety harness correctly and connecting it, via an energy-absorbing lanyard, to a suitable anchor point.
From Working at height: A brief guide, The Health and Safety Executive
Working at height: A brief guide (hse.gov.uk)

## Slide 4: Types of access equipment
Ladders
Mobile towers
Hop ups
Steps
Scissor lift
Cherry picker
Tubular

## Slide 5: Access equipment
Equipment | Main features | Safety checks
Step ladder | Ideal for confined spaces. Four legs give stability. | Knee should remain below top of steps. Check hinges, cords or ropes. Position only to face work.
Ladder | Ideal for basic access, short-term work. Made from aluminium, fibreglass or wood. | Check rungs, tie rods and/or repairs. Ensure it is placed on firm, level ground. Angle should be no greater than 75° or 1 in 4.
Mobile mini towers or scaffolds | These are usually made from aluminium and are foldable with lockable wheels. | Ensure that the ground is even and the wheels are locked. Never move the platform while it has tools, equipment or people on it.
Mobile tower scaffolds | These are larger versions of mini towers, usually with added edge protection. | Ensure that the ground is even and the wheels are locked. Never move the platform while it has tools, equipment or people on it. Base width to height ratio should be no greater than 1:3.

## Slide 6: Access equipment
Fixed scaffolds and edge protection | Scaffolds fitted and sized to the job with edge protection and guard rails. | There must be sufficient braces, guard rails and scaffold boards. The tubes should be level. There should be proper access using a ladder.
Mobile elevated work platforms | Known as scissor lifts or cherry pickers. | Specialist training is required before use. Use guard rails and toe boards. Care needs to be taken to avoid overhead hazards such as cables.

## Slide 7: Working at height: ladders
Lean ladders safely: correct 75⁰ angle (one unit out for every four up).
User to maintain three points of contact at all times.
Secure ladder/anti-slip feet/lockable hinges.
Take into account weather and ground conditions.
Inspect and maintain properly prior and during use.

## Slide 8: Ladders
Incorrect - overreaching and not maintaining three points of contact
Correct - user maintaining three points of contact
Incorrect - steps
side-on to work activity
Correct - steps
facing work activity

## Slide 9: Working at height: what can go wrong?
Scaffold collapsing.
Persons falling from height.
Items and equipment falling from height.
Contact with low or sharp parts of the structure i.e. ends of scaffold poles, exposed bolt threads, etc.
Ladder collapsing or falling.
Fall from the access ladder.

## Slide 10
Any questions?