## Slide 1: PowerPoint 9: Install single-lap roof coverings
PowerPoint presentation 1.1
Unit 101: Introduction to the Built Environment
Unit 111: Roofing occupations

## Slide 2: Ridge line – mortar formation
When bedding wet fix ridge tiles it is important to remember the mortar must have the correct consistency and strength.
One problem with bedding ridge tiles is that they have a tendency to wander, so striking a line can help to keep them straight, ensure sufficient lap is maintained and will provide a consistent guide for accurate bedding.

## Slide 3: Ridge line – mortar formation
Basic technique
Position the first tile so it is central, with equal lap on to the tiles on both sides and mark the edge with a trowel to provide bedding lines.
Work the mortar in the bucket or board so you can deliver it in a neat compacted shape, slightly inside the lines.
Place a full trowel of mortar at the end, press a piece of broken tile onto it and bed on again so the shape is slightly higher than the ridge tile.

## Slide 4: Ridge line – mortar formation
Knock down the ridge tile until the clearance is about 10mm above the roof tiles and is consistent on both sides.
Once you are happy with the first ridge tile, insert a piece of broken tile in readiness for the next mortar joint then fill with a consistent width of about 15mm and place the edge bedding for the next tile.

## Slide 5: Dry fix ridge systems
Installation processes
Roll-out
Vented
Non-ventilation
Air flow
Practical demonstration from tutor
Note: always follow manufacturers’ instructions as they can differ.

## Slide 6: Ridge ends
There are various different methods of finishing ends to the ridge, depending on the system used.
How can ridge ends be finished?
Bed and point
End caps
Security fix
Block ends

## Slide 7
Any questions?