## Slide 1: PowerPoint 1: Safety planning and preparation
PowerPoint presentation
Unit 112: Construction operations and civil engineering operations

## Slide 2: Before work begins
Follow risk assessments and safe systems of work
A risk assessment is the careful study of work to be done to identify the risks to health and safety of the persons who are going to do it, to decide how those risks can be eliminated, or avoided, or decide what control measures are needed so that the work can be done safely and minimising the risks to health.

## Slide 3: Risk assessments
Follow the five steps
Step 1 – Identify the hazards.
Step 2 – Decide who might be harmed and how.
Step 3 – Evaluate the risks and decide on precautions.
Step 4 – Record your findings and implement them.
Step 5 – Review your assessment and update if necessary.

## Slide 4: Hazards
Common hazards on construction sites
Faults in equipment and tools
Stored substances
Dangerously stacked materials
Materials obstructing safe access, or simply a lack of site safety
Falls
Falling objects
Electricity

## Slide 5: Method statements – safe systems of work
A method statement is a useful way of recording the hazards involved in a specific work task and communicating the risk and precautions required to all those involved in the work.
Key points
The statement need be no longer than necessary to achieve these objectives effectively.
The statement should be clear and illustrated by simple sketches where necessary.
Avoid ambiguities or generalisations, which could lead to confusion.
Statements are for the benefit of those carrying out the work and their immediate supervisors and should not be overcomplicated.
Equipment needed for safe working must be clearly identified and available before work starts.
Workers should know what to do if the work method needs to be changed.

## Slide 6: Manual handling controls
Elimination: eliminate manual lifting of heavy flags.
Total mechanical solution: ensure flags are always handled and laid mechanically ( e.g. with vacuum lifters and mechanical grabs).
This is the preferred solution for the majority of new builds and many refurbishment works.

## Slide 7: Manual handling controls
Partial mechanical solution: ensure that the maximum possible part of the process of handling flags is done mechanically ( e.g. using mechanical solutions to get the flags near to their final position such as off-loading using a hoist).
The risk from manual handling may be reduced by using smaller/lighter flags and/or block paving.

## Slide 8: Manual handling controls
Manual handling: in rare cases, where none of these solutions is possible, smaller areas of flags may be laid manually.
Workers should be trained in lifting safely: use kinetic lifting methods, always try to walk paving slabs.
The use of lighter weight flags, or devices which allow two people to share the lift, will further reduce the risk of injury.

## Slide 9: Housekeeping
Housekeeping is a major issue for safety in the workplace. Daily trips, slips, falls and cuts result from poor housekeeping. Slips and trips are the most common cause of major injuries at work: 95% of major slips result in broken bones and they can be the initial cause for other accidents, such as a fall from height. Slips and trips are responsible for, on average:
• over a third of all reported major injuries • 20% of over-3-day injuries to employees • 2 fatalities per year • 50% of all reported accidents to members of the public that happen in workplaces • enormous cost to employers and the health service • incalculable human cost. https://www.hse.gov.uk/slips/introduction.htm

## Slide 10: Housekeeping
It is not just good enough to have a walkway around your work area. It must be kept clear, with no trailing wires, no obstructions or leftover waste materials.
You need to have ‘a see it, sort it’ attitude to ensure these and other work areas are kept clear and left clean and tidy during and at the end of the working day.
Remember ‘A tidy job is a good job’

## Slide 11: Personal protective equipment (PPE)
What is PPE?
PPE is equipment that will protect the user against health or safety risks at work. It can include items such as safety helmets and hard hats, gloves, eye protection, high-visibility clothing, safety footwear and safety harnesses.
PPE should be used as a last resort. Wherever there are risks to health and safety that cannot be adequately controlled in other ways, the Personal Protective Equipment at Work Regulations 1992 require PPE to be supplied.

## Slide 12: The hazards and types of PPE
Eyes
Hazards: chemical or metal splash, dust, projectiles.
Options: safety spectacles, goggles, face-shields, visors.
  Note: Make sure the eye protection has the right combination of impact/dust/splash/eye protection for the task and fits the user properly.

## Slide 13: The hazards and types of PPE
Ears
Hazards: semi-permanent or permanent deafness.
Options: earplugs, ear defenders or alternative method.
Note: Make sure when using earplugs that they are clean and inserted correctly, only use clean earplugs.

## Slide 14: The hazards and types of PPE
Head
Hazards: impact from falling or flying objects, risk of head bumping, hair entanglement.
Options: A range of helmets and hard hats.
Note: Some safety helmets incorporate or can be fitted with specially-designed eye or hearing protection. Do not use head protection if it is damaged – replace it.

## Slide 15: The hazards and types of PPE
Breathing
Hazards: dust, vapour, gas, oxygen-deficient atmospheres.
Options: disposable filtering face-piece or respirator, half- or full-face respirators, air fed helmets, breathing apparatus.
Note: The right type of respirator filter must be used as each is effective for only a limited range of substances.

## Slide 16: The hazards and types of PPE
Protecting the body
Hazards: temperature extremes, adverse weather, chemical or metal splash, spray from pressure leaks or spray guns, impact or penetration, contaminated dust, excessive wear or entanglement of own clothing.
Options: conventional or disposable overalls, boiler suits, specialist protective clothing, e.g. chain-mail aprons, high-visibility clothing.

## Slide 17: The hazards and types of PPE
Hands and arms
Hazards: abrasion, temperature extremes, cuts and punctures, impact, chemicals, electric shock, skin infection, disease or contamination.
Options: gloves, gauntlets, mitts, wrist-cuffs, armlets.
Note: Barrier creams are unreliable and are no substitute for proper PPE. Wearing gloves for long periods can make the skin hot and sweaty, leading to skin problems; separate cotton inner gloves can help prevent this. Be aware that some people may be allergic to materials used in gloves, e.g. latex.

## Slide 18: The hazards and types of PPE
Feet and legs
Hazards: wet, electrostatic build-up, slipping, cuts and punctures, falling objects, metal and chemical splash, abrasion.
Options: safety boots and shoes with protective toe caps and penetration-resistant mid-sole, gaiters, leggings, spats.
Note: Footwear can have a variety of sole patterns and materials to help prevent slips in different conditions, including oil or chemical-resistant soles. It can also be anti-static, electrically conductive or thermally insulating. It is important that the appropriate footwear is selected for the risks identified.

## Slide 19
Any questions?