## Slide 1: PowerPoint 5: Drainage preparation and safety
PowerPoint presentation
Unit 112: Construction operations and civil engineering operations

## Slide 2: Trench excavation
Trenches should not be excavated too far in advance of pipe laying and should always be kept to the specified design width.
Excessively wide trenches increase the amount of excavation, bedding and backfilling, and may impose a load on the pipe in excess of the design load.
Excavations for inspection chambers may need to be wider, but care should be taken to minimise their width and length.

## Slide 3: Excavation
Every year construction workers are hurt when the excavations in which they are working collapse.
Many ground types are self-supporting to some extent but a collapse can occur without warning, resulting in a person being buried, trapped, crushed or struck by a heavy mass of soil or rock.
Over the years, many deaths have occurred in both shallow and deep excavations.

## Slide 4: Planning
Before digging any excavation, it is important that it is planned to cope with the following hazards:
collapse of the sides
materials falling onto people working in the excavation
people and vehicles falling into the excavation
contact with underground services.

## Slide 5: Planning
Your supervisor should make sure the necessary equipment you might need (trench sheets, props, baulks etc.) are available on site before work starts.
Remember that unless you have good evidence to suggest otherwise you should regard the ground beside the excavation as an area to be kept free from additional loads.
As a rule of thumb for unsupported excavations, use the depth of the trench as the size of the safety zone each side.

## Slide 6: Excavation collapse
Prevent the sides and the ends from collapse by battering them to a safe angle or supporting them with timber, sheeting or proprietary support systems.
Do not go into unsupported excavations.
Never work ahead of the support.
Remember that even work in shallow trenches can be dangerous. You may need to provide support if the work involves bending or kneeling in the trench.

## Slide 7: Materials falling into excavations
Do not store spoil or other materials close to the sides of excavations. The spoil may fall into the excavation and any extra loading will make the sides more likely to collapse.
Make sure that the edges of the excavation are protected against falling materials. Provide toe boards where necessary.
Wear a hard hat when working in excavations.

## Slide 8: People and vehicles falling into excavations
Take steps to prevent people falling into excavations. If the excavation is 2m or more deep, or 1m where water is likely to collect, provide substantial barriers.
Where vehicles have to tip material into excavations, use stop blocks to prevent them from over-running.
Remember that the sides of the excavation may need extra support.
www.youtube.com/watch?v=EIthR6akGtw&list=PL079B0FC4AD2A0887
Link to Web

## Slide 9: Avoiding underground services
Your supervisor should always aim to minimise the possibility of risk to anyone who is involved in work that exposes them to contact with underground services.
When excavating, you should always follow a safe system of work that is based on obtaining as much information as possible about buried services before excavation work begins. You should use that information to ensure the work is carried out safely.

## Slide 10: Safe system of work
The person supervising excavation should have the service plans and understand how to read them.
Look around for obvious signs of underground services, e.g. valve covers or patching of the road surface.
Use a Cable Avoidance Tool (CAT) to trace any services and mark the ground accordingly.
Everyone carrying out the work should know about safe digging practices and emergency procedures.

## Slide 11: Safe digging practices
Hand dig trial holes to confirm the position and depth of cables and use a locating device even while you dig, you may have missed a cable.
Do not use ANY hand held power tools to dig within 500mm of a marked electricity cable and avoid use below surface level.
Do not hold on to or stand on exposed services to stabilise yourself or pull yourself out of a hole.

## Slide 12: Safe digging practices
Do not handle exposed services.
Do not use bricks, flint, concrete or similar materials to backfill a hole, use fine materials e.g. sand.
Report any damage, even if it seems to have had no effect on the service.

## Slide 13: Avoiding underground services
In general the services fall into three categories: pipes, cables and ducts.
Gas and water were originally constructed of cast iron but are being replaced or relined with plastic piping.
Electricity, phone and CCTV are supplied via overhead wires or underground cables.
Cable systems are either laid direct in the ground or installed in a network of ducts.

## Slide 14: Recommended depths of services
Electricity HV & LV
HV 600mm - LV 450mm
Gas
600mm
Water
900mm
Street lighting
450mm
Cable television
250mm
British Telecom
350mm

## Slide 15: Electricity
Most electricity cables are coloured black, though some high voltage cables are red. Where ducts are used they are normally coloured black if of modern plastic construction.
Protection tiles are placed above the cable, these are made out of concrete, clay or plastic. When marker tapes are used, they are usually coloured yellow with a black text. Sizes of cables range from 10mm to 100mm diameter.

## Slide 16: Gas
Gas pipes were traditionally made of iron or steel, sometimes encased in black bitumen or black PVC. During the 1970s new steel service pipes were encased in yellow PVC sheathing and yellow polyethylene pipe came into increasing use.
During the 1980s yellow polyethylene pipe became the most commonly used material for gas mains and services. Ducts range from 50mm to 300mm.

## Slide 17: Water
Water mains are normally laid at a depth of 750mm to 900mm to avoid freezing in cold weather. Older water services were laid in lead, copper galvanised steel or black polyethylene (20mm to 450mm plastic ducting) .
Now most water service pipes are laid in blue polyethylene pipes, ducts, marker tapes when used are also coloured blue.

## Slide 18: Street lighting
These are normally black armoured cable, Sizes range from 10 to 75mm. Newer cables are normally 300 to 450mm deep, and often have a marker tape laid 150mm above them, they are usually coloured orange.
Electricity is supplied from the electricity companies or local authorities.

## Slide 19: Cable television and BT
Telecoms and cable can be copper, or fibre optics and are currently laid in PVC duct that may be coloured grey (BT), or green (cable TV). Older duct may be clay, asbestos cement, iron or pitch fibre.
The duct ranges in size from 25mm to 110mm.

## Slide 20
Any questions?