## Slide 1: PowerPoint 2: Site protection planning and types
PowerPoint presentation
Unit 112: Construction operations and civil engineering operations

## Slide 2: Planning
Risk assessment should decide how the perimeter will be defined, what type will be needed to protect the public and where it should be placed.
Factors to consider will include:
the nature and type of the construction work
how heavily populated the area is
who will need to visit the site during the work
whether the site may attract children
site characteristics.

## Slide 3: Hazards causing risk to the public
Many hazards have the potential to injure members of the public and visitors. Consider what hazards exist on your project and how you will manage them.
Falling objects: you must make sure objects cannot fall outside the site boundary. On scaffolds you can achieve this using toe-boards, brick guards and netting. You may also need fans and/or covered walkways.
.

## Slide 4: Falling objects and deliveries
You must make sure objects cannot fall outside the site boundary. On scaffolds you can achieve this using toe-boards, brick guards and netting. You may also need fans and/or covered walkways.
Make sure pedestrians cannot be struck by vehicles entering or leaving the site.
Obstructing the pavement during deliveries may force pedestrians into the road, where they can be struck by other vehicles.

## Slide 5: Storing and stacking materials
You can reduce the risks associated with the storage of materials by storing materials within the site perimeter, preferably in secure compounds or away from the perimeter fencing.

## Slide 6: Openings and excavations
People can be injured if they fall into excavations, manholes, stairwells or from open floor edges.
You will need to put up barriers or covers.

## Slide 7: Other hazards
Slips, trips and falls within pedestrian area
Plant machinery and equipment
Hazardous substances
Electricity and other energy sources
Dust, noise and vibration
Road works

## Slide 8: Vulnerable groups
The elderly, children and people with certain disabilities may need special consideration.
Work in premises such as schools and hospitals requires careful thought and planning.
Some children are drawn to construction sites as exciting places to play. You must do everything you can to keep them out of the site and away from danger.

## Slide 9: Vulnerable groups
The following specific steps are particularly relevant to child safety.
Secure sites adequately when finishing work for the day.
Barrier off or cover over excavations and pits.
Isolate and immobilise vehicles and plant and, if possible, lock them in a compound.

## Slide 10: Vulnerable groups
The following specific steps are particularly relevant to child safety.
Store building materials (such as pipes, manhole rings, and cement bags) so that they cannot topple or roll over.
Remove access ladders from excavations and scaffolds.
Lock away hazardous substances.

## Slide 11: Warning notices
Used: most construction sites.
Installed: usually screwed or nailed to any solid surface, can be cable tied to fences etc.
Maintained: must be kept clean and visible at all times.

## Slide 12: Temporary signs and barriers
Used: around shallow holes and excavations. Gives operatives and pedestrians warning and safe passage.
Installed: placed by operatives and weighed down with sand bags.
Maintained: make sure visibility strips are clean. Also check during and at the end of the working day for correct position and that they are still upright.

## Slide 13: Temporary metal fencing
Used: on larger construction sites.
Installed: placed by operatives, fence panels are place into feet blocks and secured with brackets.
Maintained: check during and at the end of the working day for correct position and that they are still upright.

## Slide 14: Solid hoardings
Used: on larger high profile construction sites.
Installed: can be purpose made for particular sites, concreted into the ground and fixed in a variety of ways.
Maintained: check during and at the end of the working day for correct position, no signs of damage or access made other than correct entrances.

## Slide 15: Recap
The type and amount of site protection depends on:
the nature and type of the construction work
how heavily populated the area is
who will need to visit the site during the work
whether the site may attract children
site characteristics.

## Slide 16
Any questions?