## Slide 1: PowerPoint 20: Tonnage calculations
PowerPoint presentation
Unit 112: Construction operations and civil engineering operations

## Slide 2: Calculations
Many construction workers shy away from carrying out calculations of quantities, but it is an important part of the job.
Failing to calculate the correct amount of materials needed for a task could lead to running out of materials before completion.
Calculating quantities of materials accurately is important since mistakes can lead to unnecessary expense and inefficiency.

## Slide 3: Working out quantities
Within construction and civil engineering we use a variety of construction materials.
We calculate the different materials in different ways and formulas.
This session we are going to look at tonnage calculations. These are used to calculate sand, gravel and sub bases.

## Slide 4: Quantities
Tonnes: follow this formula
Cubic metres into tonnes = volume x density
Every material has a density.
It is how much a cubic metre of material weighs.

## Slide 5: Density of materials
Sand = 1.8
Gravel = 2.1
Granular sub base (GSB) = 2.1
Note: a good rule of thumb is to always work on sand having a depth of 50mm and GSB having a depth of 100mm when carrying out calculations.

## Slide 6: Quantities – sand
For example:
An area measures 10m x 50m and you want cover it with 50mm of sand.
First work out the area then the volume and multiply it by the density of the material.
10 x 50 x 0.050 x 1.8 = 45 tonnes of sand
L W D Density

## Slide 7: Quantities – granular sub base
For example:
An area measures 10m x 50m and you want to cover it with 100mm of GSB.
First work out the area then the volume and multiply it by the density of the material.
10 x 50 x 0.100 x 2.1 = 105 tonnes
L W D Density

## Slide 8: Now try these
How much SAND and GSB would be needed for the following areas?
23m long 6m wide
50m long 3m wide
45m long 5m wide
34m wide 47.4m long

## Slide 9: Practice makes permanent!
Complete the activities on the worksheet provided.

## Slide 10
Any questions?