## Slide 1: PowerPoint 9: Modular paving tools and equipment
PowerPoint presentation
Unit 112: Construction operations and civil engineering operations

## Slide 2: Pins and lines
You need pins and lines to set out, keep and lay your work to the correct levels or falls. It is quite easy to lay different materials as it is a repetitive skill but the difficult part is laying and following lines and levels.

## Slide 3: Tapes and rules
Tapes and rules are another important member of the essential tool kit. You should always carry a tape measure. They come in many sizes, usually from 3m to 50m lengths and tapes are made with plastic or steel cases with steel or fibre measure.

## Slide 4: Hammers
The club or lump hammer is a handy little hammer available in a few basic weights: ranging between 2lb (0.9kg) and 4lb (1.8kg). A 2lb or 2½lb (1.1kg) is the most comfortable to work with but the 4lb is handy when working with heavier materials, such as natural stone. They can have either a wooden or fibreglass shaft.

## Slide 5: Mallets
Small rubber mallets are ideal for persuading small flags into place. They are perfect for more delicate work, such as block paving and edging kerbs.
Mallets are available in different sizes, colour and weights.

## Slide 6: Rubber mauls
These originally were made from timber but now are made from rubber. They are 6kg (13¼lb) in weight and used to knock down large element paving. Sometimes written as 'Mall', which seems to be a shortened form of 'Mallet', they are definitely pronounced ‘Maul’ rather than ‘Mal’. The shafts, like most modern tools, can be either timber or fibreglass handles.

## Slide 7: Trowel
These come in a variety of sizes and shapes depending on use! The handles can be wooden or soft grip.
Generally, for laying paving you would use a bricklaying type trowel for spreading and preparing the sand or mortar beds. Always make sure they are clean after use.
Pointing trowel are used for filling in joints and pointing certain types of joint. They are available in different sizes and need cleaning like the brick trowel.

## Slide 8: Trowels/floats
Trowels or floats come in a variety of shapes, sizes and even the material that they are made from.
Steel floats with soft, plastic or wooden handles are used for smoothing the bedding layer when the screed doesn't quite fit.

## Slide 9: Levels
These are made from aluminium and available in various sizes from 225mm to 1200mm in length. They are used for levelling things horizontally and for plumbing vertically. Some levels have an adjustable bubble at the bottom for levelling angled work. We also use a small hanging level for setting falls and transferring levels over small distances.

## Slide 10: Straight edge
Straight edges are used to check levels and heights, also transferring heights and levels to other parts of the job. They can be an offcut of timber or purpose-made metal feathered edges.
This tool is not to be underestimated as without checking your job with straight edges or levels it can quickly start to twist and run out. Also, the timber lengths make excellent screeds.

## Slide 11: Hand saw
This is mostly used for cutting the timber lengths down to size and the notches required when cutting the timber screed.
These are available in various sizes and makes etc. The one shown has an integral 45 and 90 degree angle built into the handle, universal tooth cuts with and across the grain and hard point teeth.

## Slide 12: Shovels
These come in a variety of shapes and sizes. The ‘Square-mouth’ is a handy tool for scooping and levelling, with its wide business end.
However, it's not as good as a ‘Taper-mouth’ for digging, especially in hard or clay ground.
Square-mouth
Taper-mouth

## Slide 13: Rakes
The rake is used for spreading and raking materials evenly over a large surface area. It can be made with a tubular steel shaft with teeth and has an overall length of 1500mm and head of 400mm.

## Slide 14: Wheelbarrow
Wheelbarrows are primarily used for transporting materials around construction sites. They are simple to use and operate. Top tips for use:
Always face the wheelbarrow in the direction of travel before filling.
Try to put the majority of the load over the wheel as it keeps it lighter and lets the wheel do the work – not you.
Different types are available: solid, pneumatic wheeled or even puncture resistance, plastic, steel or galvanised bodies.

## Slide 15: Brush or broom
The sweeping brush or broom is a very important tool. A tidy job is a good job. It is also used to brush the grout to seal the paving slabs.

## Slide 16: Cut off saw – petrol or electric
These are used for cutting paving in virtually any shape or size needed with ease. There are different blades to suit the job required. You must be well trained and deemed competent before using these.

## Slide 17: Block splitter
This is an excellent piece of equipment that cuts block paving down to size. It is safer than an electric or petrol cut off saw as it produces no noise or dust.
The only thing is to make sure to keep the blades sharp or the cuts are not as accurate.

## Slide 18: Vibrating plate
This is used to compact the base layer and sometimes to compact the surface of paved areas. Use a rubber mat to protect the surface finish. They are available from various manufacturers and come in different weights.

## Slide 19
Any questions?