## Slide 1: PowerPoint 12: Concrete materials
PowerPoint presentation
Unit 112: Construction operations and civil engineering operations

## Slide 2: Materials
Concrete is a product made of the following materials:
Cement
Aggregates –
– fine aggregate which is sand
– coarse aggregate which is gravel
Water

## Slide 3: Cement
Cement is the most important material in concrete as it is this that binds the aggregates together to provide strength and durability.
Several types of Portland cement, previously known as Ordinary Portland Cement (OPC), have been developed over the years. As well as Portland cement there are cements for rapid hardening, cements for sulphate resistance and white cement for architectural finishes and what are termed composite and combination cements

## Slide 4: Aggregates
The term 'aggregate' is used to describe the gravels, crushed rocks and sands that are mixed with cement and water to make concrete. As aggregates form the bulk of the volume of concrete and affect its performance, the selection of suitable material is important.
Fine aggregate (sand) includes natural sand, crushed rock or crushed gravel that is fine enough for substantially all to pass through a sieve with 4mm gaps. Coarse aggregate comprises larger particles of gravel, crushed gravel or crushed rock.

## Slide 5: Aggregates
Be aware: there is a lot of variation of aggregates available.
The gravel used in concrete should be angled to give greater strength.
The sand used should be sharp sand also known as concreting sand.
Quartz
Pigment
Sand
Sand
Sand
Pea gravel
Granite

## Slide 6: Sizes of aggregate
The maximum size of coarse aggregate is governed by the type of work to be performed. For reinforced concrete it should be such that the concrete can be placed without difficulty, surrounding all reinforcement thoroughly, particularly in the cover zone, and filling the corners of the formwork. It is usual in the UK for the coarse aggregate used for reinforced concrete to have a maximum nominal size of 20mm.

## Slide 7: Sizes of aggregate
Smaller aggregate, usually 10mm, may be needed for concrete that is to be placed through congested reinforcement. In this case, the cement content may have to be increased by 10–20% to achieve the same strength and consistence, because the fine aggregate content and water content normally have to be increased to produce a consistent mix.

## Slide 8: Water
Water is an essential component of concrete required to hydrate the cement, a process where the water chemically combines with the cement to make it harden.
The water used for mixing concrete should be free from any impurities that could adversely affect the process of hydration and, consequently, the properties of concrete.

## Slide 9: Water quality
Drinking water is suitable and it is usually simple to obtain a supply from the local water utility. Recycled water is being increasingly used in the interests of reducing the environmental impact. Seawater is not suitable for reinforced concrete or concrete containing embedded metal.
A good rule to follow is to use water that is potable i.e. good enough to drink.

## Slide 10: Admixtures
An admixture is a material, usually a liquid, which is added to a batch of concrete during mixing in order to modify the properties of the fresh and/or hardened concrete. Admixtures are now used in most concrete.
Admixtures benefit concrete by reducing the amount of free water required for a given level of consistence, often in addition to some other specific improvements, including pumping, placing, strength, durability and sustainability.

## Slide 11: Admixtures
There are occasions when the use of an admixture is not only desirable but also essential. Because admixtures are added to concrete in small quantities, they should be used only when a high degree of control can be exercised.
Incorrect dosage of an admixture – either too much or too little – may adversely affect the strength and other properties of the concrete.

## Slide 12: Materials
When all of the materials are mixed together this starts the setting process. The setting and hardening of cement results from a chemical reaction between cement and water, not from a drying process.
This reaction is called hydration . It produces heat and is irreversible. Setting is the gradual stiffening whereby the cement paste changes from being a wet and workable material into a hardened state.
YouTube Link

## Slide 13: Mixing
The most important operation when mixing concrete is the gauging of the materials.
This will ensure that:
the same mix is achieved every time.
the correct mix is used as specified by the designer.

## Slide 14: How is this done?
The most accurate way of gauging a mix is to use gauge boxes. This will ensure that the correct volume of each material is used (i.e. sand, gravel and cement). A typical concrete mix would be 1 part cement, 2 parts sand and 4 parts gravel. This is known as a 1 :2: 4 mix.
If a specification details a 1 :2: 4 mix, the information that is being communicated to you is called a ratio.

## Slide 15: Gauging the materials
The easiest way to gauge the materials is by using buckets or gauge boxes. Buckets are more readily available so we will concentrate on them.
Example: if we were mixing a batch of concrete to a 1:2:4 ratio we would measure out the materials dry by filling the bucket 4 times with gravel, then 2 times with sand and once with cement.

## Slide 16: Mixing
Concrete may be mixed by hand, by machine (mixer) or ready mixed.
Remember it is very important to wear the correct PPE when handling, using or mixing Concrete.

## Slide 17: Mixing with a mixer
Again, following the rules regarding gauging, place the materials in the machine and add the water in stages.
When mixing materials by machine it is important to remember that they should be mixed for a minimum of 2 minutes to ensure full amalgamation of the materials.
But you must also remember over mixing can cause segregation of the aggregates.
https://www.youtube.com/watch?v=T_gepV_KDnk
YouTube Link

## Slide 18: Ready mixed
Using ready mixed concrete has many advantages.
Saves time, effort and money.
Reduces space needed on site (compared to mixing in-situ).
Guarantees the same mix.
Can be ordered in any amount.
Many types of mixes available.

## Slide 19
Any questions?