## Slide 1: PowerPoint 11: Modular paving construction methods paving slabs
PowerPoint presentation
Unit 112: Construction operations and civil engineering operations

## Slide 2: Typical cross-section of a paved area
A typical paved area is made from three layers of construction.
The bottom or first layer called the sub-base.
The second is called the bedding layer.
The third is the surface course.

## Slide 3: Preparing the area
The area to be paved should be carefully marked out in preparation before excavation begins.
Always try to keep this area as square as possible. Work out where the water is going to fall to once the paving is installed. Ideally this is to an existing drain or soak to the natural watercourse.
A good rule of thumb is to excavate down to a solid base; this is normally a clay-type material.
Video link: www.youtube.com/watch?v=EEfLN42zaAw&list=PL30E0467B279E05A4
YouTube Link

## Slide 4: Falls
Paving provides a paved surface that is virtually impermeable. Flags with mortared joints are resistant to water penetration immediately after setting.
Sand-filled joints develop water resistance in early life. A flag pavement therefore requires gradients for drainage of surface water. Minimum crossfalls of 2.5% (1:40) and longitudinal falls of 1.25% (1:80) are recommended, wherever possible.

## Slide 5: Tolerances
The flag pavement should be laid to the following tolerances. The finished surface level tolerance from the design level of the flag pavement should be ± 6mm.
Adjacent flags should not differ in level by more than 3mm.

## Slide 6: Laying the sub-base
The heights and falls of the path/patio should have set out by a competent person ensuring that there will be no ponding of water on the finished surface.
The sub-base material should be spread and levelled to the desired heights and falls with either a shovel or rake as needed.
The typical thickness of the sub-base generally should be no less than 75–100mm. This should then be compacted with a vibrating plate.
If you were using a vibrating plate that weighed 1400kg/m2 to 1800kg/m 2 then you would need to pass over the layer six times with the vibrating plate to make sure it was compacted enough.

## Slide 7: Laying the sub-base layer
Video links:
Using a vibrating plate
www.youtube.com/watch?v=0YnEpeKS4_A
www.youtube.com/watch?v=3v-6o29nE7U
www.youtube.com/watch?v=fKS2K9qo-dM
YouTube Link

## Slide 8: Edge restraints
Flag paved areas must be restrained at their edges to prevent movement: either progressive movement of the whole paved area or individual flags.
Edge restraints resist lateral movement and restrict loss of laying course material at the boundaries.
Edge restraints should be laid at all boundaries of the paved area, including where the flag pavement joins different flexible materials, such as bituminous bound material.
Compaction of pavement layers near edge restraints should be delayed until any concrete bed and haunch has gained sufficient strength to prevent movement of the edge restraint.

## Slide 9: The bedding layer
Once the sub-base has been laid and compacted to the desired heights, then the next stage is constructing or laying the bedding layer.
There are various methods of constructing this layer:
Screeding on a sand bed
Hand laying on mortar bed
The method chosen largely depends upon the type of paving that is to be laid.

## Slide 10: Screeding
The material used for this method is normally sharp sand and sometimes this may be mixed with cement (depending on the construction method used).
This method is normally used for paving that has been designed to be laid this way. It is always best to use paving slabs that have been designed with small tolerance within their thicknesses.
This method normally needs the edge restraints to be set and ready to lay from. A timber screed is used to spread and level the sand to the required height. The timber is either notched at the required depth or flat on the screed poles.

## Slide 11: Sand laying course thickness
Laying course material should be spread to give a thickness of 25mm after being placed and fully compacted.
A thickness of 30mm of uncompacted material is usually suitable. A trial area should be used to determine the required surcharge.

## Slide 12: Preparation of the sand laying course
The laying course should be prepared only to the extent that work can be completed during the working day or before the onset of inclement weather. Areas of prepared laying course should not be left overnight. The laying course material should be screeded and prepared using one of the following methods: pre-compaction or partial pre-compaction.

## Slide 13: Pre-compaction
Spread out the laying course sand to a depth sufficient to give the required compacted nominal thickness after compaction of the sand and flags (the uncompacted thickness of sand will depend on the nature and moisture content of the sand and a trial area may be necessary to ascertain the surcharge).
Compact with a vibrating plate compactor and screed to level the surface, then loosen the top 10mm with a rake.

## Slide 14: Partial pre-compaction
Spread out the uncompacted laying course material to a depth approximately equal to the required compacted nominal thickness after compaction of the sand and flags. Compact with a vibrating plate compactor, then lay and screed approximately a further 10–15 mm of loose material before laying flags.
Where screed rails are used, they should be carefully removed to avoid disturbing the screeded surface of the laying course. Any depressions left by the screeding rails should be made good.
If the prepared laying course is disturbed or damaged prior to flag laying it should be re-screeded to the required tolerances.

## Slide 15: Laying paving slabs
Flags should be laid to line and level and bedded down using a pavior's maul or, for small element paving flags, a vibrating plate compactor.
It may be necessary to use a vibrating plate compactor fitted with a neoprene sole plate to protect some flags with special finishes. The installer should work from flags already placed, taking care not to disturb them. Laid flags should not be trafficked within 1.0m of an unrestrained edge.

## Slide 16: Jointing flags on a sand laying course
Flags should be laid with joints 2 to 5mm wide and fine dry jointing sand, brushed in to completely fill joints. Additional sand may be added to top up the joints as necessary after the flags are compacted with the vibrating plate compactor.
Jointing sand should preferably be kiln dried. Care should be taken to select jointing sand which does not stain the surface of the flags, where it would be detrimental to the aesthetic appearance of the pavement.
Joint filling and final compaction should be completed on the same day as laying or before inclement weather. It may be necessary to add additional jointing sand during the early life of the pavement.

## Slide 17: Hand laying
Laying course material.
The mortar should consist of freshly mixed, moist 1:3 cement-sand mortar (proportions by volume) or 1:3 lime-sand mortar (proportions by volume).
The mortar laying course should be spread out to a depth of 30–35 mm to provide a nominal 25 mm thickness after compaction.
Areas of prepared mortar laying course should be paved as soon as possible. Cement based mortar that has begun to set or has been mixed for more than two hours should be discarded.

## Slide 18: Laying flags on a mortar laying course
Areas of prepared mortar laying course should be paved as soon as possible. Cement-based mortar that has begun to set or has been mixed for more than two hours should be discarded.
The flags should be carefully laid on a full mortar bed and bedded down to line and level with a pavior's maul.
The installer should not stand in freshly laid mortar nor on freshly laid flags unless suitable action is taken to prevent movement of the laid flags.

## Slide 19: Jointing flags on a mortar laying course
Flags are laid with wide joints (i.e. 5 to 10 mm wide) and the whole of the joint should be filled with a compacted mortar to within 2 to 3mm of the flag surface using a 1:4 cement-sand (proportions by volume) mortar, containing sand complying to BS EN 12620:2002.
Flag paving containing mortar joints and/or mortar laying courses should be protected from pedestrian traffic until the mortar has achieved a working strength.

## Slide 20: Paving installation
Paving slab/flag laying should normally start at a fixed edge restraint. However, any edge restraint is unlikely to be perfectly straight or at 90 degrees to the intended flag pattern.
Therefore, a string line should be set up a short distance from the edge restraint and used to align the first row of flags. A second string line at 90 degrees to the first will ensure that the flag bond does not ‘wander’.
The area between the first string line and edge restraint can then be infilled with cut flags or concrete blocks, cut to fit as necessary. It is important to continue to use string lines during laying of the paved area to ensure joints appear visually straight or in line.

## Slide 21: Paving slabs cutting
As work progresses, the paved area should be completed with any necessary cut flags inserted and bedded, followed by compaction and jointing.
Flags may be cut using a saw, bolster and chisel or a suitable disc cutter. Small element paving flags may also be cut using a suitable mechanical flag splitter.
Take care to ensure a safe working environment during any cutting operation and that all procedures conform to the relevant safety legislation.

## Slide 22: Video links
Start to finish: mortar bed method
www.youtube.com/watch?v=ZvEIZLQgN1U
www.youtube.com/watch?v=8J3kx7JMLTk
www.youtube.com/watch?v=k73_AB3v1yE
www.youtube.com/watch?v=WwR2RhYxZ-o
www.youtube.com/watch?v=90iMrLGLODo
www.youtube.com/watch?v=CLHRcUUm7bc
YouTube Link

## Slide 23: Video links
Screeding method
www.youtube.com/watch?v=_jwWvTfdQZA
www.youtube.com/watch?v=zMwg0xGjft8&list=PL99B9420DBA73CA86
www.youtube.com/watch?v=ciKN0xPjlWY&list=PL99B9420DBA73CA86
YouTube Link

## Slide 24
Any questions?