## Slide 1: PowerPoint 10: Modular paving construction methods block paving
PowerPoint presentation
Unit 112: Construction operations and civil engineering operations

## Slide 2: Typical cross-section of a paved area
A typical paved area is made from three layers of construction.
The bottom or first layer called the sub-base.
The second is called the bedding layer.
The third is the surface course.

## Slide 3: Preparing the area
The area to be paved should be carefully marked out in preparation before excavation begins.
Always try to keep this area as square as possible. Work out where the water is going to fall to once the paving is installed. Ideally this is to an existing drain or soak to the natural watercourse.
A good rule of thumb is to excavate down to a solid base; this is normally a clay-type material.
Video link: www.youtube.com/watch?v=EEfLN42zaAw&list=PL30E0467B279E05A4
YouTube Link

## Slide 4: Falls
Paving provides a paved surface that is virtually impermeable when new.
Sand-filled joints develop water resistance in early life. A block paved area therefore requires gradients for drainage of surface water. Minimum crossfalls of 2.5% (1:40) and longitudinal falls of 1.25% (1:80) are recommended, wherever possible.

## Slide 5: Laying the sub-base
The heights and falls of the block paving should be set out by a competent person ensuring that there will be no ponding of water on the finished surface.
The sub-base material should be spread and levelled to the desired heights and falls with either a shovel or rake as needed.
The typical thickness of the sub-base generally should be no less than 75–100mm. This should then be compacted with a vibrating plate.
If you were using a vibrating plate that weighed 1400kg/m2 to 1800kg/m2 then you would need to pass over the layer six times with the vibrating plate to make sure it was compacted enough.

## Slide 6: Laying the sub-base layer
Using a vibrating plate:
www.youtube.com/watch?v=0YnEpeKS4_A
www.youtube.com/watch?v=3v-6o29nE7U
www.youtube.com/watch?v=fKS2K9qo-dM
YouTube Link

## Slide 7: Edge restraints
The paved area must be restrained at its edges to prevent movement, either of the whole paved area or individual blocks. Edge restraints resist lateral movement, prevent rotation of the blocks under load and restrict loss of laying course material at the boundaries.
Edge restraints should be laid at all boundaries of the block paved area including where block paving abuts different flexible materials, such as grassed areas.

## Slide 8: The bedding layer
The sharp sand (ideally double washed sand) should be screeded and prepared using one of the following methods:
Pre-compaction of laying course: spread the material in one layer and compact using a plate compactor, making allowances for the reduction in thickness achieved during compaction and level the surface by screeding.
Un-compacted laying course: spread the material loosely in a uniform layer and screed to the thickness required to give the target laying course thickness after the paving blocks have been laid and vibrated into place.
www.youtube.com/watch?v=Z-Au0RnKgmg
YouTube Link

## Slide 9: Laying the surface course
Block laying should normally start at a fixed edge restraint.
If this edge restraint is unlikely to be adequately straight or at 90 degrees to the intended block bond, a string line temporary datum should be set up a short distance from the edge restraint and used to align the first ‘row’ of blocks.
A second string line at 90 degrees to the first will ensure that the block bond does not ‘wander’. The area between the first string line and edge restraint can then be infilled with blocks, cut to fit as necessary.
It is advisable to continue to use string lines or other control methods during laying of the paved area.

## Slide 10: Laying the surface course
The blocks should be laid with joint widths between 2–5 mm, in the specified bond. The spacer nibs on some blocks are not designed to fix the joint width but rather to prevent damage to the blocks from face-to-face contact. For hand laying, the installer should work from blocks already placed, taking care not to disturb them. Full blocks should be laid first using an open laying face as shown:

## Slide 11: Block laying patterns
Precast concrete paving blocks are manufactured in an array of shapes, sizes and colours enabling numerous patterns and designs.
For pedestrian areas, the laying pattern is not as important as in trafficable areas. For vehicular trafficked areas, the most effective laying pattern is herringbone bond.

## Slide 12: Stretcher bond
Stretcher bond is suited to pedestrian areas and very lightly trafficked areas not subject to regular turning movements or frequent braking or acceleration. Block rows should be laid at right angles

## Slide 13: Basket weave
This pattern is suited to pedestrian areas only and should not be used for trafficked areas.

## Slide 14: Herringbone patterns
Herringbone patterns are suitable for all applications.
Herringbone at 90º to an edge
Herringbone at 45º to an edge

## Slide 15: Block cutting
Before the end of the working day, or the onset of inclement weather, the block paved area should be completed, as far as practicable, with the insertion of cut blocks, followed by the bedding operation, joint filling and compaction.
Blocks should be cut using a hydraulic or mechanical block splitter, saw or abrasive disc cutter, to an accuracy that ensures a joint width between 2–5 mm.
Cut blocks may be used up to one-third of their original length. Cut blocks smaller than a quarter of their original length should not be used.
Cutting the blocks longitudinally should be avoided, as the resultant cut piece may be significantly weaker than a full-width block.
www.youtube.com/watch?v=8nwT43nKhlI
YouTube Link

## Slide 16: Joint filling
Before the commencement of the joint filling operation the block layer should be checked to ensure that it is in full compliance with the specification, including levels and tolerances, joint spaces and block alignment, and with any non-conformance corrected.
Fine, dry (preferably kiln dried), free-flowing silica sand in accordance with the following (based upon the new European Aggregate Standard, BS EN 12620 - fine category f2) should be brushed into the joints between the blocks, fully filling the joints.
This operation is followed by two or more applications of the vibrating plate compactor. Additional sand should be added to top up the joint as necessary after compaction and during the early life of the pavement. The sand selected should not stain the surface of the paving.

## Slide 17: Video links
www.youtube.com/watch?v=rrwERw-UESY
www.youtube.com/watch?v=uNh74o7ifW8
www.youtube.com/watch?v=J__TVDrOzgo
YouTube Link

## Slide 18
Any questions?