## Slide 1: PowerPoint 8: Modular paving materials
PowerPoint presentation
Unit 112: Construction operations and civil engineering operations

## Slide 2: Subbase or granular sub base (GSB)
The sub-bases/foundation layer in the construction of patios and footpaths of block paving.
Store in bays which have separating walls to avoid mixing.
The floor of these bays should be concrete and have a slight fall towards the front of the bins to allow free drainage of rain water.
What’s it used for?
How is it stored?

## Slide 3: Sharp sand
Laying paving slabs and blocks on. Or use in a mix for concrete.
Store in bays which have separating walls to avoid mixing.
The floor of these bays should be concrete and have a slight fall towards the front of the bins to allow free drainage of rain water.
What’s it used for?
How is it stored?

## Slide 4: Silica sand
Filling in the small gaps in block paved areas.
Store on pallets to keep the bags clear of the floor and away from walls to allow a good circulation of air.
Always keep this sand dry.
Never store bagged materials more than eight high.
What’s it used for?
How is it stored?

## Slide 5: Cement
This is the binder glue when making mortar/bedding layer or concrete when laying paving.
Must be stored in well-ventilated, waterproof sheds – preferably with timber floors.
Cement should be stored on pallets to keep the bags clear of the floor and away from walls to allow a good circulation of air.
Never store bagged materials more than eight high to avoid compaction or 'warehouse setting'
What’s it used for?
How is it stored?

## Slide 6: Timber edging
Used as an edge restraint on a footpath.
Used for cutting screeds for the bedding layer when laying blocks.
Delivered in small and large quantities and are generally banded together.
Should be stored on cross bearers to stop warping and kept flat.
What’s it used for?
How is it stored?

## Slide 7: Edging kerbs or boot kerbs
Normally used as an edge restraint on a footpath.
Store on a pallet.
Shrink wrapped when possible; if stored loose, should be stacked on edge to avoid damage to their arrises.
What’s it used for?
How is it stored?

## Slide 8: Paving slabs
As a surface finish on paths, patios and footways; various sizes are available.
Store on a pallet.
Shrink wrapped when possible; if stored loose, should be stacked on edge to avoid damage to their arrises.
What’s it used for?
How is it stored?

## Slide 9: Block paving
As a surface finish on roads and footways.
Store on a pallet.
Shrink wrapped when possible; if stored loose, should be stacked on edge to avoid damage to their arrises.
What’s it used for?
How is it stored?

## Slide 10
Any questions?