## Slide 1: PowerPoint 13: Concrete formwork and reinforcement
PowerPoint presentation
Unit 112: Construction operations and civil engineering operations

## Slide 2: Formwork
The purpose of formwork is to contain freshly placed and compacted concrete until it has gained enough strength to be self-supporting, produce a concrete element of the required shape and size, and to produce the desired finish to the concrete.

## Slide 3: Requirements of formwork
The formwork should be sufficiently rigid to stop it moving during the placing of the concrete.
It should be of sufficient strength to carry the weight or pressure of the wet concrete.
It should be set to line and level within the specified tolerances.
Joints should be sufficiently tight to prevent loss of water or cement paste from the concrete.

## Slide 4: Types of formwork: site
Road forms ( Steel forms) are quite popular among professional contractors for use on site as it is sturdy and tough, more than capable of withstanding the rough and tumble of a busy construction site and virtually unbreakable. It can be re-used time and time again, requires little skill to set-up and is cheap – single lengths can be hired for less than a couple of pounds per week.

## Slide 5: Types of formwork: site
Timber shuttering is more traditional and, while the steel form is the formwork of choice for simple slabs, there are situations where it is simply not possible or feasible to use it, so timber shuttering is used.
The great advantage of timber shuttering over steel form is that, because it is erected on site, it can be made to accommodate any situation, ranging from odd shapes, to greater depths. Timber shuttering is also the usual choice for vertical concrete work, although it is often used in conjunction with modular steel bracing elements.

## Slide 6: Release agents
All formwork, whether it is steel road-form or timber shuttering, needs to be coated with a release agent (mould oil) before any concrete is placed.
The purpose of a release agent is to prevent the concrete bonding to the formwork and then 'scabbing' when the formwork is removed. It also helps to ensure the formwork stays clean and free from concrete, so that it can easily be re-used elsewhere.
It is normally a liquid which is painted onto the formwork in advance of the concrete being poured and it dries, leaving behind a soapy or waxy residue that has no deleterious effect on the concrete.

## Slide 7: Striking of formwork
The period which should pass before the formwork is struck will vary from job to job and will depend on the concrete used, the weather and the exposure of the site, any subsequent treatment to be given to the concrete, the method of curing and other factors.
Formwork must not be removed until the concrete is strong enough to be self-supporting and able to carry imposed loads. Thus, the time of striking should be related to the strength of the concrete, and obviously soffit forms to beams and slabs must be left in place longer than is necessary for the side forms. However, where appearance is important, striking times should be as consistent as possible to ensure the least colour variation in the finished surface.

## Slide 8: Reinforcement – why the need?
Concrete has good compressive strength, but is brittle and will not take shear stress, bending moments or tensile stress.
The steel reinforcement helps to keep it from cracking if it is subjected to stresses other than compression.

## Slide 9: Reinforcement
Reinforcement for concrete may consist of deformed steel bars or welded steel fabric. These materials are covered by BS 4449, 4482 and 4483. The requirements for scheduling, dimensioning, bending and cutting of reinforcement are covered by BS 8666.
Prefabricated reinforcement
It is often more convenient to obtain cages and complex reinforcement arrangements already assembled from the supplier's factory. Delivery can be timed to fit in with the construction programme but the same requirements for storage on site apply as for conventional reinforcement. Some of the assemblies are heavy and will need suitable lifting equipment.

## Slide 10: Cover to reinforcement
The strength, durability and fire resistance of a reinforced concrete structure depend on, among other factors, the reinforcement being correctly positioned, within allowable tolerances, in the hardened concrete.
The most common cause of corroding reinforcement is insufficient cover (inadequate concrete quality is another major cause). The position of reinforcement should be checked before and during concreting to ensure that the correct cover is maintained.
Spalling from lack or incorrect cover

## Slide 11: Cover to reinforcement
To stop spalling occurring there should be nominal cover to the reinforcement and this is normally given on the working drawings.
Nominal cover is the depth of concrete cover, shown on drawings, to the reinforcement nearest to the surface of the concrete, including links.
The nominal cover will depend on the conditions of exposure of the particular element of concrete and the cement content, cement type and free water/cement ratio of the specified concrete.

## Slide 12: Keeping the cover – spacers and chairs
The cover to reinforcement can be achieved by using spacers and chairs to BS 7973-1, positioned in accordance with BS 7973-2.
Spacers are made of plastic, fibre cement or concrete, and are supplied in several shapes and various sizes to give the correct cover. Chairs are used to space layers of reinforcement the correct distance apart. They are used in slabs and walls.

## Slide 13: Spacers and chairs
Spacers and chairs must be durable, and not cause corrosion of the reinforcement or spalling of the concrete. Those made from fibre-cement or concrete should be comparable in strength, durability, porosity and appearance if the finish of the surrounding concrete is important. Site-made concrete blocks must not be used. More guidance on using spacers is given in publication BS 7973.

## Slide 14: Fixing reinforcement
The reinforcement bars should be securely tied together with soft iron wire or tying devices in accordance with BS 7973. Care should be taken to ensure that projecting ends of ties or clips do not intrude into the concrete cover.
Structural connections between bars are usually made by lapping. Mechanical couplers can be employed if lapping is not feasible or if long lap lengths would cause unacceptable congestion. If there is any uncertainty about the arrangement of the reinforcement, or any discrepancy between the bar schedules and the drawings, the engineer should be consulted.

## Slide 15: Videos
Step liners https://www.youtube.com/watch?v=QuqryhFu9w8
Timber form work www.youtube.com/watch?v=yD4xNFDZvcA
Plastic forms www.youtube.com/watch?v=MK7qBFYau6U
Modular formwork systems https://www.youtube.com/watch?v=S-wFwXw4jUQ
Formwork to column and beams www.youtube.com/watch?v=D8MMTrXsWB0
YouTube Link

## Slide 16
Any questions?