## Slide 1: PowerPoint 3: Site protection boundaries
PowerPoint presentation
Unit 112: Construction operations and civil engineering operations

## Slide 2: Planning
Risk assessment should decide how the perimeters will be defined, what type will be needed to protect the public and where it should be placed.
Factors to consider will include:
the nature and type of the construction work
how heavily populated the area is
who will need to visit the site during the work
whether the site may attract children
site characteristics.

## Slide 3: What you need to do
The law says you must conduct your business without putting members of the public at risk. This includes the public and other workers who may be affected by your work.
The project client or co-ordinator should provide information about:
boundaries
adjacent land usage
access
measures to exclude unauthorised persons.

## Slide 4: Authorisation
The principal contractor must take reasonable steps to prevent unauthorised people accessing the site.
People may be authorised to access the whole site or be restricted to certain areas.
You must explain relevant site rules to authorised people and do any necessary site induction.
You may need to supervise or accompany some authorised visitors while they are on site or visiting specific areas.

## Slide 5: All construction sites require
Measures to manage access through defined boundaries
Steps to exclude unauthorised people.
While the numbers of children being killed or injured on construction sites has reduced, there is no room for complacency. Each year, two or three children die after gaining access to building sites, and many more are injured.

## Slide 6: Site boundaries
You need to define boundaries physically, where necessary, by suitable fencing. The type of fencing should reflect the nature of the site and its surroundings.
Determining the boundary is an important aspect of managing public risk.
You need to carry out PPM
Planning what form the perimeter will take
Providing the fencing/hoarding and
Maintaining the fencing/hoarding.

## Slide 7: Planning
What is the nature and type of the construction work?
How heavily populated is the area is?
Who will need to visit the site during the work?
Will the site attract children?
What are the site characteristics? (Think about existing site boundaries, location, proximity to other buildings.)

## Slide 8: Providing
Typically, in populated areas, this will mean a two-metre high small mesh fence or hoarding around the site.

## Slide 9: Types of fencing

## Slide 10: Types of fencing

## Slide 11: Hoardings
The location and type of construction affects the type protection chosen. If the construction project needs to be more secure because of its location, then hoardings will typically be chosen.
Hoardings have come a long way from the basic timber construction. It is now common for hoarding to be colourful, informative, have lighting and include viewing platforms.

## Slide 12: Types of hoardings

## Slide 13: Types of hoardings

## Slide 14: Types of hoardings

## Slide 15: Types of hoardings

## Slide 16: Maintaining
You need to make sure that all boundaries, perimeters are checked:
before starting work
throughout the working day
the end of the working day.

## Slide 17
Any questions?