## Slide 1: PowerPoint 20: Hydronic heating part 5
PowerPoint presentation
Unit 113: Plumbing, heating and ventilation

## Slide 2: This session:
In this session we will look at I&C heating system installations and some of the methods used to install larger-scale heating systems.
1.6 – The types and layout features of heating systems

## Slide 3: Industrial and commercial heating systems
So what’s the difference between a domestic and an I&C system?
Simple – the scale is the biggest difference.
The quantity of water, pressures and heat inputs required for large-scale buildings mean that different strategies may need to be considered.
The multiple zones within large buildings means that more complex control systems are needed and multiple circuits for different building areas may be required.
The heat emitters (which we will discuss in later sessions) may be different.
But … remember, the principle of LTHW (Low Temperature Hot Water) and hydronic heating systems remains the same, both domestic and I&C systems can be open vented or sealed and pressurised.

## Slide 4: Low Temperature Hot Water systems (LTHW)
The term central heating tends to be replaced by the term LTHW when discussing the distribution of heat through pipework in commercial buildings.
LTHW (hydronic heating systems operating below 100⁰C) is used for:
Space heating to radiators and a range of heat emitters
Supplying heat to ventilation systems such as Air Handling Units (AHUs)
Providing heat to produce hot water by exchanging its heat into a heat exchanger (calorifier)
For larger scale (such as hospitals) and industrial systems – MTHW (100⁰C–120⁰C) and HTHW (150⁰C plus) may also be used.

## Slide 5: I&C systems – scale
I&C systems contain huge amounts of water and need to be able to produce large quantities of heat. Therefore, the boiler needs to be bigger.
This may be one or two large boilers or multiple smaller boilers coupled together to work in sequence, known as modular boilers.

## Slide 6: I&C systems – scale
Boiler power (or output) is measured in kilowatts (kW)
Typically a domestic boiler is rated at between 25–30 kW
An I&C boiler is generally rated at 70kW plus, with some larger boilers rated at over a mW … that’s 1000 kW!
Not only is the boiler bigger, but so also are:
The fuel supply
The distribution pipework
The heat emitters

## Slide 7: I&C systems – zones
Zoning of a system can be complex so let’s look at the principle … imagine a large school building.
One part of the school may be warmer than another due to having more sun on it or because it is closer to a kitchen.
The heat into these areas should be controlled to avoid wasting heat by giving each area the same amount – some of which may not be needed.
A common method of managing this is by using multiple flow and return circuits from the boiler room. Let’s take a look.

## Slide 8: I&C systems – zoning
These modular boilers are connected to a ‘low loss header’
The header is used to allow multiple connections to different circuits – in this system you can see the header is connected to two zones, each controlled by its own three-port valve
Boiler shunt pump moves water from boilers to header
Three-port valve controls the heat in each zone
Heat output at zone 1 to radiators or other type of heat emitter
Heat output at zone 2 to radiators or other type of heat emitter
Variable temperature circuit pumps used to move water around each individual circuit

## Slide 9: I&C systems – low loss headers
Gas pipe
Low loss header
Pump fitted on
the return pipework

## Slide 10: Pre-fabrication
On large I&C installations, it is common to fabricate pipework sections away from the site.
Many sites do not allow hot work such as welding, brazing and soldering to take place onsite.
Therefore, they are produced offsite and are transported to site before fitting in position.

## Slide 11
Any questions?