## Slide 1: PowerPoint 8: Sources of water
PowerPoint presentation
Unit 113: Plumbing, heating and ventilation

## Slide 2: This session:
In this session we will discuss the sources of water in Wales and England and the different qualities these sources offer:
1.1 – The key stages in the rainwater cycle
1.2 – The various sources of water and the typical properties of water from those sources
1.3 – Underground sources: deep and shallow wells, Artesian wells, bore-holes, springs

## Slide 3: The rainwater cycle
Water moves constantly, in what is scientifically known as the hydrological cycle.
We know this by its more common name – the rainwater cycle.
This natural process is where water is continually exchanged between the atmosphere, the Earth’s surface, the ground and plants.
River running back to the sea to restart the process
Rain and snow
Water saturated cloud
Water vapour
Heat from the sun
Evaporation

## Slide 4: The rainwater cycle
Evaporation – when water molecules move apart.
Precipitation – when water molecules condense and fall as rain.
Oceans and seas evaporate
Clouds in the sky
Rain falls on land
Rivers flow

## Slide 5: Cold water use
BES engineers have a responsibility to design, install, test and maintain cold water systems correctly.
We also need to advise customers on good usage.
Bathing and showering – 25.4%
Flushing toilets – 21.8%
Using a hand basin – 12.2%
Washing clothes – 11.7%
Other household use – 11.4%
Washing dishes – 8.3%
Gardening – 5.6%
Cooking and drinking – 3.6%

## Slide 6: Sources of water
  There are two main sources of water:
  Surface sources – including upland surface water, artificial reservoirs, and rivers and streams
  Underground sources – including wells, artesian wells and springs
Notes: 6

## Slide 7
Sources of water – surface water
Lakes
Reservoirs
Canals
Rivers

## Slide 8
Sources of water – underground sources: deep well
Lake
Deep well
Land spring Unconfined aquifer Shallow well
Impervious strata
Impervious strata
Pervious strata
Confined aquifer
Impervious strata

## Slide 9
Sources of water – Underground sources- Artesian well
Water bearing strata
Artesian spring Artesian well
Impervious strata
Impervious strata
Plane of saturation

## Slide 10: Sources of water
  Water is stored by water companies – either in its untreated state in impounding reservoirs or lakes, or as wholesome water in service reservoirs.
  Water must be treated before it is put into the supply system:
    Deep wells and bore holes – quality of water is quite good, due to the natural filtering process; only requires sterilisation treatment.
    Rivers, lakes and reservoirs – usually dirty and polluted; treatment process usually involves the water being strained, filtered, chemically treated and sterilised.
    Wholesome water – water which is clean and suitable for drinking. Also known as potable water!
Notes: Remind learners that:
it is the responsibility of water companies to ensure water is wholesome (fit to drink)
how water is treated will depend on its source and what impurities it contains
sterilisation serves to keep both the water and supply pipework free from bacteria as the water is piped into our homes.
10

## Slide 11
Water resources in Wales are managed by one of five water companies. These are:
Dŵr Cymru Welsh Water (DCWW)
Hafren Dyfrdy (HD),
Severn Trent Water
Albion Water and
Southern and Scottish Energy Water (SSE Water)
Approximately 95% of the water in Wales originates from surface water.
Sources of water
Let’s take a look here at the list of reservoirs in Wales and England.

## Slide 12: Types of water
As it falls to the ground, it can absorb carbon dioxide to produce a weak solution of carbonic acid.
If sulphur trioxide is present in the atmosphere, it can become a very weak sulphuric acid.
When water leaves the cloud as rain, hail or snow, it is almost pure and contains very few impurities.
The effect of these contaminants on the water quality.
Water (H2O) leaves the cloud as rain, hail, sleet and snow
As the rain, hail, sleet and snow falls from the cloud, it absorbs contaminants such as carbon dioxide and sulphur trioxide becoming mildly acid water dissolving
more salts, minerals and gases on the ground
SO3
CO2
SO3
CO2
SO3
CO2
SO3
CO2
SO3
CO2
SO3
CO2
SO3
CO2
SO3
CO2
SO3
CO2
CO2 SO3 CO2
SO3 CO2 SO3
CO2 SO3 CO2
Sandstone contains CO2
Soft water
Very soft water
Permanently hard water
Temporary hard water
Moorland peat more CO2 added
Calcium carbonate (limestone) CaCO3
Calcium sulphate (salt)

## Slide 13: Hard and soft water
Temporarily hard water can cause many problems within plumbing systems. If hard water is heated above 65⁰C, it loses its calcium. If you look at a kettle in a hard-water area, you’ll see that a layer of limescale has built up on the inside of the kettle.
When limescale builds up in plumbing and heating systems, the following problems can occur:
the limescale insulates the water from the heat source, resulting in bad heat transfer which wastes fuel and means a longer heating-up time
the limescale may block heat exchangers and pumps, causing localised boiling as the water cannot move away from the heat exchanger fast enough and the water boils momentarily. This is known as ‘kettling’.

## Slide 14
Any questions?