## Slide 1: PowerPoint 7: Producing offsets
PowerPoint presentation
Unit 113: Plumbing, heating and ventilation

## Slide 2: This session:
In this session we will discuss the process of making an offset in copper pipe:
2.2 – How to select and safely use hand tools and power tools
3.1 – How to measure and mark out for fixings to pipework and plumbing and heating components
3.4 – The methods for the bending of pipework used in BSE
3.5 – The requirements for the installation of pipework
5.1 – Follow safe working procedures
5.2 – Measure, mark and cut pipework materials for installation

## Slide 3: Offset bends
Offsets are useful to help pass pipe over raised obstructions and other services. Let’s take a look at the process:
Step 1: To find the correct offset angle, the size of the offset should be deducted from the 600mm and the 600mm folding rule opened to the measurement, i.e. offset 50mm. 600 – 50 = 550
Offset measurement
Offset measurement 50mm
Angle required
600mm rule

## Slide 4: Offset bends
Step 2: Bend the tube to the angle set by the rule.
Offset measurement 50mm
Angle required
600mm rule

## Slide 5: Offset bends
Step 3: Remove the tube from the machine and mark for the second bend measuring from the inside edge of tube using a straight edge.
Bending mark
Straight edge
Offset measurement

## Slide 6: Offset bends
Step 4: Reposition tube in the machine so that the mark forms a tangent to the former.

## Slide 7: Offset bends:
Step 5: Reposition the rule to give the correct angle for the second bend.

## Slide 8
Any questions?