## Slide 1: PowerPoint 5: Common fixing devices, clips and brackets
PowerPoint presentation
Unit 113: Plumbing, heating and ventilation

## Slide 2: This session:
In this session we will learn about other methods available to join copper pipe:
2.1 – The work in the BSE occupations trade area
2.2 – How to select and safely use hand tools and power tools
2.4 – The clip and bracket types used in BSE
2.6 – Common fixing devices for pipework
3.1 – How to measure and mark out for fixings to pipework and plumbing and heating components

## Slide 3: Fixing devices – screws
There are many types of screws available for different applications:
countersunk
crosshead
pozidrive
raised countersunk
round head
mirror
coach
Chipboard.
Screws can be made from steel, stainless steel or brass, and come with a range of screw head types.
They can be coated with corrosion protection such as bright zinc and black japanned coatings.
Screws are specified by their length in millimetres or inches, and their gauge.
gauge
length

## Slide 4: Materials and surfaces
Brickwork Generally an outside finish, uneven and hard.
Blockwork
A hidden internal fabric (first fix). Plastered or rendered.
Wood Commonly floorboards or lining finish.
Studwork
Hidden after first fix by plaster board
Plasterboard Soft fabric finish requiring painting.
Tiling
A hard, decorative finish to bathrooms, WCs, kitchens and floors.

## Slide 5: Common screws
New fixing technologies are being developed all the time, take a look at these masonry fixings here.
 | Countersunk screw – Used for general work. The head sinks flush or a little below the wood surface. Needs a flat blade-type screwdriver.
 | Crosshead/Pozidriv screw (countersunk type) – Used for general work and very similar in appearance to the countersunk screw, but needs a crosshead screwdriver. This ensures that the screwdriver does not slip out of the screwhead. Ideal for pipe clips.
 | Raised countersunk screw – Used for fixing decorative fittings with countersunk holes. The head is designed to be visible.
 | Round head screw – Used for fixing copper saddle clips.
 | Mirror screw – Used for fixing mirrors and bathroom fittings such as bath panels. The chromed cap threads into the screw head to hide the screw.
 | Coach screws – These usually come with purpose- made wall plugs. They are used for fixing heavy constructions such as boilers. Can be tightened with a spanner but some have Pozidriv screw heads.
 | Chipboard screw – Used for securing chipboard and medium density fibreboard (MDF). Various types of heads are available.

## Slide 6: Screw heads
Flat blade For use with slotted screws. Care should be taken to ensure the correct blade size for the screw slot. | 
Phillips head Originally designed in the 1930s to intentionally ‘ride-out’ of the screw head to prevent over-tightening. | 
Pozidriv head Similar to the Phillips head but has an eight-pointed star shape for better grip. Not compatible with Phillips screws. | 
Star head Not often used, except in specialist installations and appliances. Also known as Torx screwdrivers. | 
Hexagon head (Allen key) Mainly used in the gas industry for appliance servicing and installation. | 

## Slide 7: Fixings and components – plasterboard fixings
Expanding plastic wall plug
Expanding metal cavity fixing
Spring toggle fixing
Self-cutting fixing (self-tapping screw)

## Slide 8: Fixings and components – masonry fixings
Rawl bolt
Self-tapping wall bolt
Fischer bolt basin set

## Slide 9: Fixings and components – standard wall plugs
Standard plastic wall plugs:
Yellow plugs: drill bit size = 5mm, screw gauge = 6–8
Red plugs: drill bit size = 6mm, screw gauge = 8–10
Brown plugs: drill bit size = 7mm, screw gauge = 10–14

## Slide 10: Pipe clips and brackets – Domestic use
Nail clip
Single and double push-in clip
Single and double clip lock
Single copper saddle clip
Single stamped brass school board clip
Single cast brass school board clip
Brass Munsen ring clip (adjustable)

## Slide 11
Malleable iron Munsen ring and back plate
Malleable iron school board clip
Pressed steel bracket
Rubber lined steel bracket
Pressed steel bracket with phenolic block
Pipe clips and brackets – Industrial and Commercial

## Slide 12: Steel pipe support systems
There is a large range of manufacturers of steel support and bracket systems that work well with drop brackets and screwed rod bracketing systems.
Take a look at these videos:
Trapeze bracket
Gripple suspended brackets

## Slide 13
Any questions?