## Slide 1: PowerPoint 21: Hydronic heating part 6
PowerPoint presentation
Unit 113: Plumbing, heating and ventilation

## Slide 2: This session:
In this session we will look at district heating systems.
1.6 – The types and layout features of heating systems
So what is a district heating system? Take a look at this video.

## Slide 3: District heating
District uses heat produced centrally.
This is supplied to both industrial and residential customers, using either steam or high temperature hot water via heat networks.
Networks of highly insulated pipes travel in ducts and trenches to buildings where heat is transferred to individual systems via plate heat exchangers.
This is a system that local governments are increasingly investing in to prevent high carbon emissions, particularly in built-up areas.

## Slide 4: District heating
To add to the environmental advantage of these systems, CHP (Combined Heat and Power) plants are used to produce the heat as a bi-product of the electrical generation process.
District heating is centred on one large heat source running very efficiently.
This is preferred over each building having separate smaller ones running less efficiently.
It reduces overall CO2 emissions and saves on running costs.

## Slide 5: District heating
Transformer
Heat exchanger
Domestic properties
Electrical distribution station
Power supply
Flow
Return
Services distribution
Stack
Generator
Control panel
Gas turbine
Natural gas supply
Thermal store

## Slide 6: District heating
The high pressure, high temperature primary water produced at the central plant transfers its energy within Heat Interface Units (HIU) within individual properties – often flats or apartments.

## Slide 7: District heating
A range of ‘hydraulic separation’ methods are then available. Here CH and HW plate heat exchangers (PHE) are used for each circuit.

## Slide 8: District heating
Advantages:
Reduced CO2
No need for fuel supply within property
Ideal for flats and apartments in built up areas
Helps government reach green targets
Reduced maintenance costs within property (no fuel)
Disadvantages:
If the central plant fails, all properties are without heat

## Slide 9
Any questions?