## Slide 1: PowerPoint 17: Hydronic heating part 2
PowerPoint presentation
Unit 113: Plumbing, heating and ventilation

## Slide 2: This session:
In this session we will identify the differences between one- and two-pipe systems. We will look at the terminology and methods used to control heating and hot water systems within domestic dwellings and small commercial properties.
1.6 – The types and layout features of heating systems

## Slide 3: Two-pipe heating systems
This system differs considerably from the one-pipe system in having two pipes, a flow and a return, which are connected to the boiler.
Radiators are connected to separate branches of the main flow and return pipes.
Each radiator has its own flow and return pipework to the boiler.
All heat emitters achieve the same temperature.
Two-pipe arrangement
One-pipe arrangement

## Slide 4: Two-pipe semi-gravity system
Same basic principle as the one-pipe semi-gravity. In this system, the heating has a thermostat fitted to control space temperature.
15mm cold feed pipe
22mm vent pipe
Boiler
22mm flow and return
Room thermostat controlling the pump
Programmer
28mm gravity
primaries
Feed and expansion cistern

## Slide 5: Two-pipe semi-gravity heating system
A two-pipe system is much better than a one-pipe system, but even the two-pipe semi-gravity is not yet compliant with Building Regulations.
For this we need to improve the system controls.
ADVANTAGES
DISADVANTAGES
All of the heat emitters reach the same temperature.
The two-pipe system is much quicker at heating up than the one-pipe system. This saves on fuel usage.
Uncontrolled heating of the primary circuit leads to overheating of the domestic secondary hot water.
Constant boiler cycling even when the hot water and heating are up to temperature leads to wastage of fuel energy.
The system is not compliant with Building Regulations Document L and must be updated to a C-Plan system as a minimum standard.
The boilers fitted to this type of system are only about 78 per cent efficient or lower.
Condensing type boilers cannot be fitted to this type of installation because of the gravity circulation needed by the hot water storage cylinder.

## Slide 6: Control of heating systems
Central heating
Time clock
Boiler
Control is very important in heating systems. Excessive temperature within the system can be dangerous and the Building Regulations advise us that we need to conserve energy.
Look at these two systems we have covered.
What is the difference in control?
Boiler
Room thermostat controlling the pump
Programmer

## Slide 7: Control of heating systems
Central heating
Time clock
Boiler
One-pipe system – heating and hot water has no temperature control except the boiler thermostat
Two-pipe system – has room thermostat to control room temperature, but hot water temperature is still controlled by boiler thermostat
Both systems have time control.
Boiler
Room thermostat controlling the pump
Programmer

## Slide 8: Control of heating systems
It is essential then that domestic heating and hot water systems have suitable controls for time and temperature.
Modern systems are normally controlled by what is known in industry as ‘Honeywell Plans’.
These are individual methods of connecting and wiring controls for small Commercial and Domestic systems. Common plans include:
C–Plan (minimum standard for existing systems)
Y–Plan (heating & DHW fully pumped by a circulating pump and includes 1 x 3 port valve)
S–Plan (also fully pumped and includes 2 x 2 port valves)

## Slide 9: Honeywell plans: C–Plan
Motorised valve
Boiler
Room thermostat
Pump
Programmer
15mm cold feed pipe
Wiring centre
Cylinder thermostat
28mm gravity primaries
The C-Plan (two-pipe) semi-gravity system has total thermostatic control with the inclusion of a room thermostat and a cylinder thermostat linked to a single two-port motorised zone valve on the gravity flow before it enters the heat exchanger on the storage cylinder, the system must include controls to prevent boiler cycling.

## Slide 10: Honeywell plans: Y–Plan
This system uses a single three-port motorised mid-position valve to control the flow of water to the central heating circuit and the hot water circuit.
It is controlled by a cylinder thermostat and a room thermostat. Individual thermostatic radiator valves independently control the temperature of each room.
Automatic air valve
Programmer
Wiring centre
Cylinder Room thermostat thermostat
System bypass
Mid-position
valve
Feed and
expansion cistern
22mm vent pipe 15mm cold feed
22mm flow and return pipes

## Slide 11: Honeywell plans: S-Plan
This system uses two two-port zone valves to control the flow of water to the central heating circuit and the hot water circuit. They are controlled by a cylinder thermostat and a room thermostat. Individual thermostatic radiator valves independently control the temperature of each room.
.
Room thermostat
Programmer
Wiring centre
Automatic
air valve
System bypass
Two-port zone valve
Two-port zone valve
22mm flow and return pipes
Feed and expansion cistern
22mm vent pipe
Cylinder thermostat
15mm cold feed

## Slide 12: Summary
We have identified the difference between one- and two-pipe systems
We now know the difference between pumped and gravity circulation
We are aware that heating and hot water systems need controls to comply with the Building Regulations
We know that there are different ways of piping domestic and small commercial systems that have different control arrangements
We are now aware that these Honeywell plans include C-Plans, S-Plans and Y-Plans!

## Slide 13: Summary
 | Full thermostatic control | Compliant with Building Regulations Document L | Recommended for larger properties | Can be used with sealed (pressurised) systems | Can be used with system boilers | Can be zoned | Anti-cycling boiler interlock
Y-Plan system |  |  | × |  |  | × | 
S-Plan system |  |  |  |  |  |  | 

## Slide 14
Any questions?