## Slide 1: PowerPoint 23: Warm air heating and space heating
PowerPoint presentation
Unit 113: Plumbing, heating and ventilation

## Slide 2: This session:
In this session we will look at the basic principles of warm air heating and, in particular, gas fired units.
1.6 – The types and layout features of heating systems

## Slide 3: Warm air heating
Warm air heating is largely used in I&C buildings, but not so much in the domestic sector in Wales.
This type of heating uses a fan that passes air over a warm heat exchanger before distributing it into the space through grilles.
The heat exchanger may be heated by LTHW (such as a Fan Coil Unit or Air Handling Unit) or directly by the heat produced by burning a fuel such as natural gas.
These gas fired warm air heaters are split into two main types:
indirect fired appliances
direct fired appliances.

## Slide 4: Gas fired warm air heaters
Gas fired warm air heaters are commonly used in large internal spaces such as:
School halls
Warehouses
Factories
Suspended gas fired warm air unit.

## Slide 5: Indirect gas fired warm air heaters
This is the most common type of heater installed.
Indirect heaters use a heat exchanger that is warmed by a gas burner.
A fan blows air across the warm heat exchanger to produce warm air.
The dangerous gases produced by the burner do not get pushed into the heated space.
Indirect gas fired warm air unit.

## Slide 6: Direct gas fired warm air heaters
The direct gas fired heaters are less common and more widely used in agriculture such as nurseries and large-scale greenhouses.
They do not contain a heat exchanger and therefore the products of combustion are forced into the heated space.
In the production of crops, this is actually a benefit as they contain CO2!
Suspended direct fired units in a greenhouse facility.

## Slide 7: Radiant tube heaters
Another popular space heating method is the radiant tube heater.
This gas fired appliance uses radiant heat emitters to warm surfaces and people below it rather than the air itself.
The benefit of this is that warm air can rise to high points and be lost through openings such as doors in warehouses. The radiant tube heater only ‘spot heats’ the solid surfaces below it, using radiation.

## Slide 8
Any questions?