## Slide 1: PowerPoint 18: Hydronic heating part 3
PowerPoint presentation
Unit 113: Plumbing, heating and ventilation

## Slide 2: This session:
In this session we will discuss microbore heating systems and the main principles behind underfloor heating systems.
1.6 – The types and layout features of heating systems

## Slide 3: Microbore heating systems
The microbore system is a form of two-pipe system that uses a very small-bore pipe to feed the heat emitters.
Uses a multi-connection fitting (manifold) fitted to the flow and return pipes, which are normally 22mm or 28mm.
All flow pipes to heat emitters taken from flow manifold and all returns to the return manifold.
Heat emitters supplied through microbore pipework, generally 8mm or 10mm in diameter.
Manifolds fitted in pairs with the flow and return manifolds beside each other.

## Slide 4: Microbore heating – system layout
In small dwellings all the radiators may be taken from one pair of manifolds, which can accommodate up to eight radiators.
It is usual to fit a separate pair of manifolds on each floor in a house, and larger properties may have two pairs on each floor.
15mm
22mm
22mm
22mm
22mm
Manifolds connected to 8mm or 10mm microbore tubing

## Slide 5: Microbore system – advantages and disadvantages
ADVANTAGES
DISADVANTAGES
Contains only a small amount of water, so is quickly heated.
Microbore tubing comes in fully annealed coils and is easily bent by hand and easily hidden.
It can sometimes be a cheaper form of installation. Long lengths of tubing means fewer joints.
Can be used with sealed and open-vented systems, Y-Plan or S-Plan.
The system is compliant with Building Regulations Document L.
Microbore piping is easily damaged and not very resistant to knocks.
Microbore tubes can get easily blocked with sludge if the system is installed poorly.
The system can suffer from scale build-up in areas where temporary hard water exists.
Because of smaller pipework, frictional resistance is greater, which can put increased strain
on the circulator.

## Slide 6: Underfloor heating systems
Underfloor heating is a popular modern choice and is highly compatible with a range of heat sources, including high efficiency systems such as heat pumps.
A main advantage is that lower temperature flow is required to maintain room temperature due to larger heat emitter surface area.
The boiler heats the system water, which is then pumped to the underfloor heating manifold.

## Slide 7: Underfloor heating – principles
This type of heating works differently to conventional heat emitters. The floor becomes the heat emitter when it is heated up by pipework that has been laid under the screed or boards on top of insulated beds.

## Slide 8: Underfloor heating – manifold
Room temperature is maintained via thermostatically motorised actuators on the return manifold.
The manifold is at the centre of an underfloor heating system. Here water from the heat source is distributed to all individual room circuits and should be positioned as centrally in the property as possible.
Pump
Automatic air vent
Flow meter
Isolating valve
Isolating valve
Actuator head
Blending valve
Pressure gauge

## Slide 9: Underfloor heating – pipework
Typically, underfloor heating pipework is 16mm outside diameter and 12mm internal diameter, but it may vary dependent on manufacturer and specification and is available between 10mm and 20mm in diameter.
Pipework is normally a barrier type multi-layer construction and normally either Pex-Al-Pex or Pert-Al-Pert.
PEX-AL-PEX pipes can withstand up to 95ºC.
PERT-AL-PERT can withstand approximately 85ºC.
Supplied in varied length in coils of between 100m and 300m to avoid jointing. No joints should be laid within the floor unless for repair work.

## Slide 10: Underfloor heating – pipework
Pipework is laid using pre-made clips and floor trays. It can be installed in a number of different patterns.
The series pattern laid out
The snail pattern laid out

## Slide 11: Underfloor heating – system layout
Underfloor heating circuits
Two way manifold
Pump
Hot water cylinder
Pump
Boiler
Top view
Typical underfloor heating system combined with wet radiators

## Slide 12: Underfloor heating – summary
Advantages of underfloor heating include:
energy efficient when installed and designed correctly
no maintenance of heat emitters
good heat distribution throughout room
hygienic – radiators can trap dust and bacteria
aesthetic – no heat emitters on view
good for open space areas where radiators are difficult to position.

## Slide 13
Any questions?