## Slide 1
PowerPoint presentation
PowerPoint 10: Plan for common tasks
Unit 114: Electrotechnical systems and equipment

## Slide 2: Planning a sequence of work
Installing electrical wiring in building projects requires expertise and proper planning. It directly impacts the safety of the utilities/equipment and the safety of the people using them.
The scope of electrical wiring covers supply, installation, testing and commissioning of all accessories, wiring, switches, socket outlets, spur outlets, junction boxes/pull boxes, connections etc.

## Slide 3: Planning a sequence of work
  Planning the work sequence is an essential part of the overall installation process.
  When work sequences are well planned, a tight production schedule incorporating all work sequences can be created, ensuring the workflow will be maintained.
  Whether the project is a new building or a refurbishment, the electrical installations should be planned to meet the needs of the occupants. Asking some simple questions at the beginning will avoid overloading any circuits with multiple high-performance electrical appliances, or an increased use of connector strips.

## Slide 4: Questions to ask when planning
Here are a few points to think about to allow architects, builders or electrical contractors to plan and implement the correct electrical infrastructure:
Which electrical appliances do I use in each room?
Where should light sources be installed (both fixed and via sockets)?
Where are the TV, computer or telephone connections required?
Where are mobile devices usually charged and should sockets with USB ports be installed?
How do I want to control the outdoor lighting?

## Slide 5: Planning a sequence of work
You can then decide:
The number of circuits
The number of sockets
The number of lamp connections
The number of TV and communication connections

## Slide 6: Planning a sequence of work
The planning is carried out on the basis of an accurate construction plan or floor plan of the building – either in the original or on the computer with corresponding group plan software.
Pay particular attention to doors and their opening direction, windows and stairs, and steps and fireplaces.
It is useful to show furnishings in the floor plan where they will be positioned in the rooms. Once all this information has been obtained, the respective connections in the rooms can be drawn in as required.

## Slide 7: Benefits of planning
Planning will help you to:
refine your method of working as you familiarise yourself with what has to be done
develop a work sequence that minimises time spent collecting, organising and understanding the drawing requirements
organise your activities so that there will be no backtracking in search of information at a later stage
communicate with the team
complete the job on time.

## Slide 8: Example of an electrical plan

## Slide 9: Types of diagrams
    Circuit diagrams are a pictorial way of showing circuits. Electricians and engineers draw circuit diagrams to help them design the actual circuits.
    Wiring diagrams show the components of the circuit and how to make the connections between the devices. A wiring diagram usually gives more information about the relative position and arrangement of devices and terminals on the devices.
    Layout diagrams are the plan or design arrangement of an installation. They are scaled drawings and show the position of the electrical equipment to be installed.

## Slide 10: Materials list
    A materials list is a predefined list of parts that may be referenced for an installation to ensure consistent material planning for jobs.
    A list of materials is required before you start your installation, whether it is domestic, industrial or for a commercial project. The materials list will include the quantity of cables and equipment required to complete all or part of the project.
    First, define the material list header information, and then add part line items to the material list.

## Slide 11: Example of a materials list
Item name | Description | Quantity | Unit cost | Total
Prepared by: Signed by: |  |  |  | 

## Slide 12: Specifications and manufacturer’s instructions
    Installation specifications
    Installation specifications detail the work, materials and installation required to complete a project. The specifications are a subcontractor’s field guide on what materials to use, how to install them and the desired level of quality.
    Manufacturer’s instructions
    Manufacturer’s instructions provide suitable information and instructions on the installation, operation, maintenance and safe use of equipment.

## Slide 13: Risk assessment
A risk assessment is the process of evaluating risks to workers' safety and health from workplace hazards. It is a systematic examination of all aspects of the work to be done and considers:
what could cause injury or harm
whether the hazards could be eliminated and if not
what preventive or protective measures are, or should be, in place to control the risks.

## Slide 14: Example of a risk assessment
Location:
Risk assessment reference number: Review date:
Review by:
Risk Assessment
Activity / Workplace assessed: Return to work after accident Persons consulted / involved in risk assessment
Date: Reviewed on:
Significant hazard | People at risk and what is the risk Describe the harm that is likely to result from the hazard (e.g. cut, broken leg, chemical burn etc.) and who could be harmed (e.g. employees, contractors, visitors etc.) | Existing control measure What is currently in place to control the risk? | Risk rating Use matrix identified in guidance note Likelhood (L) Severity (S) Multiply (L) * (S) to produce risk rating (RR) |  |  |  | Further action required What is required to bring the risk down to an acceptable level? Use hierarchy of control described in guidence note when considering the controls needed | Actioned to: Who will complete the action? | Due date: When will the action be complete by? | Completion date: Initial and date once the action has been completed
Uneven floors | Operatives | Verbal warning and supervision | L 2 | S 1 | RR 2 | L/M/H m | None applicable | Site supervisor | Active now | Ongoing
Steps | Operatives | Verbal warning | 2 | 1 | 2 | m | None applicable | Site supervisor | Active now | Ongoing
Staircases | Operatives | Verbal warning | 2 | 2 | 4 | m | None applicable | Site supervisor | Active now | Ongoing

## Slide 15: Method statement
A method statement is a description of how the work will be carried out safely.
M E T H O D S T AT E M E N T |  |  |  |  |  |  | 
Revision Date: |  | Revision Description: |  |  |  |  | Approved By:
Work Method Description |  | Risk Assessment |  | Risk Levels |  |  | Recommended Actions* (Clause No.)
1. |  |  |  |  |  |  | 
2. |  |  |  |  |  |  | 
3. |  |  |  |  |  |  | 
4. |  |  |  |  |  |  | 
R I S K L E V E L S: | Class 1 (high) |  | Class 2 (medium) |  | Class 3 (low) | Class 4 (very low risk) | 
Engineering Details/Certificates/Work Cover Approvals: |  |  |  | Codes of Practice, Legislation: |  |  | 
Plant/Equipment: |  |  |  | Maintenance Checks: |  |  | 
Sign-off
Print Name: Signature: | Print Name: Signature: | Print Name: Signature: | Print Name: Signature:
Print Name: Signature: | Print Name: Signature: | Print Name: Signature: | Print Name: Signature:

## Slide 16
Any questions?