## Slide 1
PowerPoint presentation
PowerPoint 2: Underlying principles for electrotechnical work
Unit 114: Electrotechnical systems and equipment

## Slide 2: The main electrical principles of a circuit
Electricity is simply the movement of electrons carrying energy. As electrons move along a conductor, they can transfer some of their energy into other forms such as heat, light or movement. Electrons create charge, which we can harness to do work. Your light bulb, your television, your phone, etc., are all harnessing the movement of the electrons in order to do work.
They all operate using the same basic power source: the movement of electrons.

## Slide 3: The main electrical principles of a circuit
Conventional current assumes that current flows out of the positive terminal, through the circuit and into the negative terminal of the source. This was the convention chosen during the discovery of electricity.
Electron flow is what actually happens and electrons flow out of the negative terminal, through the circuit and into the positive terminal of the source.

## Slide 4: The main electrical principles of a circuit
With DC (direct current) the current always flows in the same direction.
This is the type of current you get when you use a battery as the voltage source.
The direction of the current depends on how you connect the battery.
The electricity that you get from the power company is not DC but AC (alternating current).
In an AC circuit the current reverses direction periodically.
AC is what you get from the power companies.

## Slide 5
Copper atom
Hydrogen atom
Electron
Nucleus – protons and neutrons
+
-
The main electrical principles of a circuit

## Slide 6
Hydrogen atom
+
-
External pressure
External pressure
+
Copper atom
-
Strong bond
Weak bond

## Slide 7: The main electrical principles of a circuit
Current = flow of electricity (amps)
Voltage = potential difference (volts)
Resistance = resistance to flow (ohms)

## Slide 8: Current flow
Current is measured in amperes (amps)
1 amp of electrical current is equal to;
6,250,000,000,000,000,000 electrons flowing in a conductor per second!
Conductor

## Slide 9: Voltage
ELECTRON FLOW
High
Low
Voltage is electrical pressure and creates current flow
A difference in pressure between two points will create flow in the direction of the lower pressure

## Slide 10: Resistance
CURRENT
Resistance reduces current flow
Resistance is measured in ohms ()
The higher the resistance, the less current that will flow
Resistance

## Slide 11: The main electrical principles of a circuit
An electrical circuit is a path or line through which an electrical current flows. The path may be closed (joined at both ends), making it a loop.
A closed circuit makes electrical current flow possible. It may also be an open circuit where the electron flow is cut short because the path is broken. An open circuit does not allow electrical current to flow.

## Slide 12: What are the components of an electric circuit?
An electrical circuit has conductors, a protective device, a switch, a load and a power source. These are the functions of each part:
Conductors: These are usually copper wires. They make the path through which the electricity flows. One piece of the wire connects the current from the power source to the load. The other piece connects the load back to the power source.
Switch: The switch is simply a small gap in the conductor where you can close or open the circuit. When the switch is closed, the circuit is closed and electricity flows.

## Slide 13: What are the components of an electric circuit?
The load: An example of a load is a light bulb that lights when the circuit is turned on.
Overcurrent protective device:
An overcurrent occurs when the current exceeds the rated capacity of that circuit or of the connected equipment (such as an appliance) on that circuit. Examples of overcurrents are by overloading the circuit, a short circuit or an earth fault.
Circuit breakers and fuses protect circuit wiring from damage caused by overcurrent.

## Slide 14: What are the components of an electric circuit?
Whenever you turn on a light, you are using an electric circuit. There are four basic parts to this circuit that all work together to provide you with the power you need:
the AC or DC energy source
a conductor in the form of a wire
an electrical load
at least one controller being a switch.

## Slide 15: What are the components of an electric circuit?
Think about what happens when you turn on a light. You push the switch. This causes electricity to flow through the wires to the power source, which will convert the energy to light or power.
Energy source: In your circuit, the power sources will provide the voltage and current to energise your device.
Conductor: this is the wiring in your home. This provides the path that the energy flows through and connects all the other parts of the circuit. Think of this as the electric power flowing through a pipe or a hose.
Switch: This is the light switch, which closes or opens the energy flow of the circuit, allowing the energy to move through so you get power.
Load: The load is the amount of electrical energy your device needs to work. Think of your TV and your electric bill; that has to do with your load.

## Slide 16: What are the components of an electric circuit?
Switch

## Slide 17: Types of circuits
There are two types of circuits: a series circuit and a parallel circuit.
What is a series connection?
The basic idea of a ‘series’ connection is that components are connected end-to-end in a line to form a single path through which current can flow:
Series connection
Only one path for current to flow

## Slide 18: Series circuits
The total resistance of the circuit is found by simply adding up the resistance values of the individual resistors:
equivalent resistance of resistors in series
R = R1 + R2 + R3 + ...

## Slide 19: What Is a parallel connection?
The basic idea of a ‘parallel’ connection is that all components are connected across each other’s leads.
In a purely parallel circuit, there are never more than two sets of electrically common points, no matter how many components are connected. There are many paths for current flow, but only one voltage across all components:
Parallel connection
These points are electrically common
These points are electrically common

## Slide 20: Parallel circuit
The total resistance of a set of resistors in parallel is found by adding up the reciprocals of the resistance values, and then taking the reciprocal of the total equivalent resistance of resistors in parallel
1 = 1 + 1 + 1
Rt R1 R2 R3

## Slide 21: Series and parallel calculations
Resistors of 15 Ω and 25 Ω are placed in series. Calculate their total resistance.
Rt = R1 + R2
Rt = 15 + 25
Rt = 40 Ω
2. Two resistors of 25 Ω and 50 Ω are connected in parallel. Calculate their total resistance.
1 = 1 + 1
Rt R1 R2
1 = 1 + 1
Rt 25 50
1 = 2 + 1
Rt 50
Rt = 50
1 3
Rt = 16.66 Ω

## Slide 22: Conductors and insulators
Conductors conduct electrical current very easily because of their free electrons.
Some common conductors are copper, aluminium, gold, and silver.
Insulators oppose electrical current and make poor conductors.
Some common insulators are glass, air, plastic, rubber and wood.

## Slide 23
Any questions?