## Slide 1
PowerPoint presentation
PowerPoint 4: Electricity generation, transmission and distribution
Unit 114: Electrotechnical systems and equipment

## Slide 2: Electricity supply
Some industrial customers requiring large amounts of electricity may be supplied direct from sub-stations at 33,000 volts.
Electricity is taken from the National Grid transmission system using 400,000 volts and 275,000 volts and reduced to 132,000 volts and lower voltages for distribution by the local electricity companies.

## Slide 3: Transmission voltages
Electricity is ‘taken’ from the National Grid via a series of appropriately located sub-stations. These will eventually transform the grid supply back down to 11 kV and then distribute electricity at this level to a series of local sub-stations situated to the centre of demand. It is their job to take the 11 kV supply, transform it down to 400 V or 230 volts and distribute this via a network of underground radial circuits to the customer. In rural areas this distribution sometimes takes place using overhead lines.
It is also at this point that we see the introduction of the neutral conductor. This is normally done by connecting the secondary winding of the transformer in star and then connecting the star point to earth via an earth electrode beneath the sub-station.

## Slide 4: Transmission voltages
High voltage distribution 11 KV
Commercial customers 400 V
Domestic customers 230 V

## Slide 5: Transmission voltages
        Power station generating at 25KV
Step up transformer
From 25Kv to 400 KV,275KV
132KV

## Slide 6: Transmission voltages
Step down transformer
132KV to 33KV
Heavy industry 33KV

## Slide 7: Transmission voltages
Step down transformer
33KV to 11KV
Light industry
11KV

## Slide 8: Transmission voltages
Step down transformer
11KV to 400/230V

## Slide 9: Transmission
Electricity is usually generated in power stations between 23,000 and 25,000 volts, then increased by substation transformers to 275,000 and 400,000 volts, and fed into the National Grid system to be transmitted, efficiently, over long distances.
Power transformers
Power station
Transmission sub-station
TRANSMISSION
GENERATION
Distribtution sub-station
COMMERCIAL AND INDUSTRIAL BUSINESS CONSUMERS
DISTRIBUTION
RESIDENTIAL CONSUMERS
DISTRIBUTION AUTOMATION DEVICES
Photovoltaic cells

## Slide 10
Any questions?