## Slide 1
PowerPoint presentation
PowerPoint 9: Common fixing and securing methods for cable and containment
Unit 114: Electrotechnical systems and equipment

## Slide 2: Common fixing and securing methods
Different types of fixing and securing methods can be used, depending on the surface. Examples include:
Plasterboard: spring toggles, wall anchors, self drilling plasterboard fixings
Brick or masonry: screw and wall plug, rawlbolt
Wood: woodscrews
Metal: nut and bolt

## Slide 3: Spring toggles
Long screw of the toggle fixing allows use in boards of various thicknesses and with thick attachements, offering maximum flexibility.
Allows easy installation for fastenings behind thick panels in very flat cavities.
Self-acting anchor with easy installation.
Wide transition beams ensure a good load distribution allowing high load-bearing capacity.

## Slide 4: Wall anchors
Wall anchors ensure that the wall can support whatever is intended to hang on it and other loads, regardless of how heavy the hanging is or the material the accessory is made of.
The type of anchor used depends on what is being fixed.

## Slide 5: Rawlplugs
Rawlplugs are small plastic fittings that grip and hold screws when they are installed into hard walls, such as brick or cement. They will prevent a screw from coming out of the wall after you install it.

## Slide 6: Rawl bolts
Rawl bolts are generally easy to use, with good load carrying capacity.
Ideal general purpose anchor bolt with excellent tolerance to variation in hole size.
The collapsible ferrule ensures positive clamping force is transmitted to the fixture.
Suitable for use in concrete, brickwork and stone.

## Slide 7: Nuts and bolts
Nuts and bolts are designed to hold two or more objects together.
They work by inserting a bolt through the two objects and then fastening a nut at the other end of the bolt.
Need to consider how the bolts are inserted into the objects and the type of nut needed to hold it together.

## Slide 8
Any questions?