## Slide 1
PowerPoint presentation
PowerPoint 3: Quantities
Unit 114: Electrotechnical systems and equipment

## Slide 2: Ohm’s Law states that: ‘The current flowing in a circuit is in direct proportion to the voltage applied, and inversely proportionate to the resistance’ This can be expressed mathematically in the following way:
I = current V = voltage R = resistance
Electrical quantities

## Slide 3: Electrical quantities
V = I x R
I = V
R
R = V
I

## Slide 4
Electrical power is measured in watts
V
I
P
Electrical quantities
P = V x I
I = P
V
V = P
I

## Slide 5: Ohm’s law calculations
Calculate the current when a p.d. of 10 V is applied to a circuit of resistance 2
I = V
R
I = 10
2
I = 5amps
What voltage would be required to cause a current of 2A to flow through a resistance of 55?
I = V
R
Therefore V = I x R
V = 2 x 55
V = 110 volts

## Slide 6: Power calculations
Calculate the power used by an immersion heater consuming 15A when connected to a 200V supply.
P = I x V
P = 15 x 200
P = 3000watts or 3kw
Calculate the current drawn by a 1500W electric kettle connected to as 230V supply.
P = I x V
Therefore I = P
V
I = 15000
230
I = 6.52 amps

## Slide 7: General quantities
The unit for distance is the metre, according to the International System of Units.
From this base unit, using a system of equations, a number of derived quantities are obtained, such as area, volume, speed and acceleration.
Some physical values for measurement are
1 centimetre (cm) = 10 millimetres (mm)
1 decimetre = 10 cm
1 metre (m) = 100 centimetres
1 metre (m) = 1000 millimetres (mm)
1 kilometre (km) = 1000 metres

## Slide 8: General quantities
In the International System of Units (SI), the standard unit of area is the square metre (written as m2).
In electrotechnical work, and in particular in reference to the size of conductors, we use mm2

## Slide 9: SI base units
Dimension | Name | Symbol
Length | metre | m
Mass | kilogram | kg
Time | second | s
Electric current | ampere | A
Thermodynamic temperature | kelvin | K

## Slide 10: SI derived units
Dimension | Name | Symbol
Area | square metre | m2
Volume | cubic metre | m3
Speed / Velocity | metre per second | m/s
Acceleration | metre per second squared | m/s2
Luminance | candela per square metre | cd m-2
Current density | ampere per square metre | A/m2
Magnetic field strength | ampere per metre | A/m

## Slide 11: SI derived units with special names
Dimension | Name | Symbol
Frequency | hertz | Hz
Force | newton | N
Energy / Work | joule | J
Power | watt | W
Electric charge | coulomb | C
Voltage | volt | V
Capacitance | farad | F
Inductance | henry | H
Electric resistance | ohm | Ω
Moment of force | newton metre | 

## Slide 12
Any questions?