## Slide 1: PowerPoint 2: Types of backgrounds used for fixing wall and floor tiles
PowerPoint presentation
Unit 116: Wall and floor tiling

## Slide 2: Aim: To introduce learners to background surfaces. Outcomes: At the end of this session, the learner will be able to: Outcome 1: Identify different types of background surfaces and the different methods, systems and materials that can be applied to receive wall and floor tiles.
PowerPoint presentation

## Slide 3: Types of backgrounds used for fixing wall and floor tiles
In construction, there are many different types of backgrounds that a wall and floor tiler will encounter, while fixing wall and floor tiles.
What is a background?
A background is any wall or floor construction that a tiler fixes wall and floor tiles to.

## Slide 4: Types of backgrounds: new and existing
Gypsum based Timber (flooring) Cement based

## Slide 5: Types of backgrounds: new and existing
      Wall and floor tiling is carried out in many different environments, including domestic, commercial and industrial types of construction (building) sites.
      These construction (building) sites provide wall and floor tiling for new housing, shops, restaurants, offices, hospitals and many other building types.
      Wall and floor tiling is also needed within existing buildings for refurbishment and renovation works.
      New and existing buildings have a variety of different building material backgrounds relating to their design.

## Slide 6: Gypsum-based backgrounds
    Gypsum is a soft mineral composed of calcium sulphate dihydrate. It is used as a fertiliser and as the main constituent in many forms of plaster and plasterboard.
In construction, gypsum is used to manufacture plasterboard and plaster (board finish, multi finish etc.). These are typical backgrounds a tiler will have to know when installing wall and floor tiles.

## Slide 7: Cement-based backgrounds
    Cement is a binder, a powdered product used in many construction compositions such as concrete, screed render and mortar for bricklaying. It constitutes a large portion of material present in cement-based tile adhesive.
The most common type of cement used is OPC (Ordinary Portland Cement).
Concrete
Screed
Render
Mortar
https://www.plasterforce.co.uk

## Slide 8: Timber-based backgrounds
    Timber is used in a wide range of applications in the construction of buildings: flooring, doors, skirting, architraves, joists and roof structures.
A tiler will often have to tile a floor which has been constructed out of timber, but must be aware that according to BS 5385‑1:2018, 6.2.3: ‘Sheets and boards subject to movement from changes in moisture content, such as plywood, chipboard, wood partial boards, etc, should not be used.’
Timber: structural floor boards
Moisture-resistant chipboard sheeting

## Slide 9
Any questions?