## Slide 1: PowerPoint 11: Protection of areas prior to wall and floor tiling
PowerPoint presentation
Unit 116: Wall and floor tiling

## Slide 2: Aim: To give learners an understanding of the range of materials used to protect surrounding areas prior to wall and floor tiling. Outcomes: At the end of this session, the learner will be able to: Outcome 1: Identify a range of different materials used to protect surrounding areas.
PowerPoint presentation

## Slide 3: Protecting surrounding areas prior to wall and floor tiling
This is needed as the wall and floor tiling trade creates a lot of dust and waste. The waste generated constitutes spillages, staining, broken and cut tiles, over-mixing of adhesive and grouts, dirty water, packaging and many other forms of waste from the process of tile work installation.
Surrounding areas where wall and floor tiling take place include bathrooms, kitchens, hallways, stairwells and living room spaces at domestic, commercial and industrial building sites.
A tiler often has to work alongside expensive fittings, fixtures and furniture. Therefore it is important to ensure, during the planning stage, that methods and materials which are needed to provide protection to the surrounding area are put in place prior to any work starting.

## Slide 4: Protecting surrounding areas prior to wall and floor tiling
Protective materials used in tiling:
low tack masking tape
cotton and polythene dustsheets
tarpaulin
corrugated plastic
protective board and hard board.

## Slide 5: Protective materials used in tiling: low tack masking tape
This is a type of tape used by tilers and painters/decorators that has weak adhesive applied to the one side.
A low tack masking tape can be applied to a painted surface to provide protection from tile adhesive staining a finished painted surface when tiling. Using tape can prevent the need to re-decorating existing walls.

## Slide 6: Protective materials used in tiling: low tack masking tape
Using low tack masking tape to protect the tile and bath when applying silicon sealant
50mm wide tape

## Slide 7: Protective materials used in tiling: dust sheets
Cotton and plastic/polythene sheeting provides protection to carpets and other floor coverings, worktops, furniture and in mixing and cutting areas.
Cotton sheets will let moisture through, where plastic sheeting provides a barrier to liquids, improving the chance of not staining what you are trying to protect.

## Slide 8: Protective materials used in tiling: tarpaulin
A tarpaulin is a heavy duty multi-use plastic sheet which can be used internally and externally. A good quality tarpaulin is hard to rip and water resistant.
Tarpaulins are used to cover materials left outside and protect them from damage by the rain and wind.
A tarpaulin can be used to protect a driveway, grassed area or patio from damage where a mixing or cutting area has been set up outside.

## Slide 9: Protective materials used in tiling: tarpaulin
Protecting materials
Protecting a grassed area
for mixing on

## Slide 10: Protective materials used in tiling: corrugated plastic
Corrugated plastic is a cheap and versatile method to provide protection to floors and work surfaces. It is lightweight, easy to cut to shape and fit, and is available in sheets and rolls.

## Slide 11: Protective materials used in tiling: protective board and hard board
These sheet materials are more expensive and harder to cut and install prior to tiling work, but provide stronger protection on wall and floor surfaces.
These sheet materials can include:
ply board
hard board
OSB (oriented strand board)
chipboard.

## Slide 12: Protective materials used in tiling: protective board and hard board
These materials provide surface protection for tiling work where there may be a chance of damaging the surface by cracking, scratching or chipping. An example could be tiling a kitchen splashback over a granite work top.
Plywood/board
Hardboard
OSB
Chipboard

## Slide 13
Any questions?